## Slide 1: Way forward for measurement gap enhancement
Intel, Alcatel-Lucent, ZTE, Nokia Networks,
Ericsson, NTT DoCoMo
3GPP TSG-RAN WG4 Meeting #76 R4-154163
Beijing, China, August 24th-28th, 2015

## Slide 2: Way forward for measurements with multiple RF chains
It is beneficial to introduce per component carrier configuration of measurement gaps
  Network controlled small gap (NCSG) can be introduced when per CC measurement gap configurations are configured to reduce the Ack/Nack missing rate due to PCell/SCell/PSCell interruption
  Benefit of multiple RF chains when gaps are configured on all CC is expected
  Detailed configurations and signaling are FFS or can be addressed in the future work item
Notes: Companies to provide use cases associated with their proposals

## Slide 3: Way forward for increased UE scheduling opportunity and/or reduced UE power consumption
It is beneficial to enhance the measurement gaps to increase UE scheduling opportunity and/or reduce UE power consumption
  Candidate proposals
    For both sync and async operation
      Burst gap pattern/periodical gap suspension (R4-154566/4754)
      Reduced MGL with configurable gap offset (R4-154160)
      Reduced Gap impact on UL scheduling (R4-154493)
      Reduced MGL with synchronized or coordinated PSS/SSS transmission (R4-153001/4365)
  Interested companies are encourage to provide evaluations in RAN4#77 on the candidate proposals at least from the following perspectives
    Inter-frequency identification delay
    Inter-frequency measurement delay
    UE scheduling opportunity for both DL and UL
      It can be equivalent to UE power consumption and/or DL/UL throughput loss due to configured gap, including both measurement gap and small gap
    Other UE and network impact, including but not limited to AGC adjustment, implementation complexity and flexibility

## Slide 4: Way forward for network controlled interruption in CA/dual connectivity
To control the interruption due to deactivated SCell measurement, NCSG and/or measurement gap (e.g. legacy 6ms gap) can be configured
  NCSG is primarily used to reduce the Ack/Nack missing rate due to PCell/SCell/PSCell interruption
  Measurement gap is primarily used for inter-frequency and inter-RAT measurement and can also be used to control the interruption