## Slide 1: Way Forward on 4Rx PDCCH performance
Ericsson,
3GPP TSG-RAN WG4 Meeting #76 R4-155199
Beijing, China, 24th – 28th Aug 2015

## Slide 2: Agreements in 4Rx Adhoc
PDCCH alignment simulations will be based on the Table on next slide
UE should not be tested under 2RX test if it supports 4RX
Introduce a “new medium” channel correlation targeting at lower correlation than the existing “medium” one. Option 1 : Beta=0.6, XPOL. Option 2 : ULA, beta =0.3874 Decide in RAN76bis between option 1 and 2 based on alignment simulations for both options and on further inputs from vendors

## Slide 3: WF on 4Rx PDCCH performance
Based on | Antenna configs | Propagation | Options of Antenna correlations
8.4.1.1 | 1x4 | ETU70 | Low
8.4.1.2.1 | 2x4 | EVA70 | Low
8.4.1.2.2 | 4x4 | EPA5 | New Medium (XPOL, Beta=0.6, Gamma=0.2 or ULA, Beta=0.3874