## Slide 1: Way forward on Maximum input level for CA_42E
CMCC

## Slide 2: Background
For CA Bandwidth class C and D, maximum input level of -25dBm for 64QAM and -27 for 256QAM are defined for the largest transmission bandwidth configuration CC, and requirement on other CC is relative to the largest one referring bandwidth
Maximum input level for Bandwidth class E is required to be defined for CA_42E
Rx Parameter | Units | CA Bandwidth Class |  |  |  |  | 
 |  | A | B | C | D | E | F
Power in largest Transmission Bandwidth Configuration CC | dBm |  | -282 | -252 | -252 |  | 
 |  |  | [-30]3 | [-27]3 | [-27]3 |  | 
Power in each other CC | dBm |  | -28+ 10log(NRB,c /NRB,largest BW) 2 | -25 + 10log(NRB,c /NRB,largest BW) 2 | -25 + 10log(NRB,c /NRB,largest BW) 2 |  | 
 |  |  | [-30]+ 10log(NRB,c /NRB,largest BW) 3 | [-27] + 10log(NRB,c /NRB,largest BW) 3 | [-27] + 10log(NRB,c /NRB,largest BW) 3 |  | 
NOTE 1: The transmitter shall be set to 4dB below PCMAX_L,c or PCMAX_L as defined in subclause 6.2.5A. NOTE 2: Reference measurement channel is Annex A.3.2: 64QAM, R=3/4 variant with one sided dynamic OCNG Pattern OP.1 FDD/TDD as described in Annex A.5.1.1/A.5.2.1. NOTE 3: Reference measurement channel is Annex A.3.2: 256QAM, R=4/5 variant with one sided dynamic OCNG Pattern OP.1 FDD/TDD as described in Annex A.5.1.1/A.5.2.1. |  |  |  |  |  |  | 

## Slide 3: Way forward
Define maximum input level requirement for CA bandwidth class E as the same way for class C and D.
Relaxation will be considered for the total maximum input level for CA bandwidth class higher than E.
Rx Parameter | Units | CA Bandwidth Class |  |  |  |  | 
 |  | A | B | C | D | E | F
Power in largest Transmission Bandwidth Configuration CC | dBm |  | -282 | -252 | -252 | -252 | 
 |  |  | [-30]3 | [-27]3 | [-27]3 | [-27]3 | 
Power in each other CC | dBm |  | -28+ 10log(NRB,c /NRB,largest BW) 2 | -25 + 10log(NRB,c /NRB,largest BW) 2 | -25 + 10log(NRB,c /NRB,largest BW) 2 | -25 + 10log(NRB,c /NRB,largest BW) 2 | 
 |  |  | [-30]+ 10log(NRB,c /NRB,largest BW) 3 | [-27] + 10log(NRB,c /NRB,largest BW) 3 | [-27] + 10log(NRB,c /NRB,largest BW) 3 | [-27] + 10log(NRB,c /NRB,largest BW) 3 | 
NOTE 1: The transmitter shall be set to 4dB below PCMAX_L,c or PCMAX_L as defined in subclause 6.2.5A. NOTE 2: Reference measurement channel is Annex A.3.2: 64QAM, R=3/4 variant with one sided dynamic OCNG Pattern OP.1 FDD/TDD as described in Annex A.5.1.1/A.5.2.1. NOTE 3: Reference measurement channel is Annex A.3.2: 256QAM, R=4/5 variant with one sided dynamic OCNG Pattern OP.1 FDD/TDD as described in Annex A.5.1.1/A.5.2.1. |  |  |  |  |  |  |