## Slide 1: WF on RF receiver requirements for 4RX AP
Ericsson
R4-155418

## Slide 2: Aim
Agree band agnostic requirements and test configurations at RAN4#76bis
Agree REFSENS for relevant bands at RAN4#77

## Slide 3: Test scope
Agreement that requirements be specified such that 2RX fall-back testing can be significantly reduced

## Slide 4: RF receiver requirements
Agreements
Maximum input level: -25 dBm (per port)
  maintain 2RX AP performance
Adjacent Channel Selectivity: same as for 2RX AP
  since relative requirement
Maintain blocker power levels and frequencies relative to band or wanted carrier

## Slide 5: For RAN4#76bis
For 4 RX AP, consider increasing the power offset between REFSENS and the wanted signal level compared to the 2RX AP case (keeping requirement1) for
in-band blocking
spurious response
For 4 RX AP, consider keeping the power offset between REFSENS and the wanted signal level compared to the 2RX AP case (tighter requirement1) for
for
out-of-band blocking
narrow-band blocking
wide-band intermodulation
Note 1: relative to the 2 RX AP case

## Slide 6: At RAN4#76bis
Decide on the offset between REFSENS and the wanted signal level for
  in-band blocking
  spurious response
  out-of-band blocking
  narrow-band blocking
  wide-band intermodulation