## Slide 1: Way forward on DB-DC-HSUPA
Qualcomm, Ericsson, Vodafone, ChinaUnicom, Huawei, HiSilicon, Ooredoo
R4-155429
TSG RAN WG4 meeting #76 Beijing, China, 24 - 28 August, 2015

## Slide 2: Background
It is agreed that DB-DC-HSUPA will be introduced for Bands I+VIII, I+V, and II+V.
RAN4 is discussing whether to introduce the following two power classes for DB-DC-HSUPA:
  Power Class 2: Max per carrier/band Tx power of 24dBm and Max UE Tx power of 27dBm
  Power Class 3: Max UE Tx power of 24dBm for sum of two carriers across both bands
    Same as in DC-HSUPA

## Slide 3: Way forward
It is agreed that UE power class 3 will be supported for DB-DC-HSUPA
The following are FFS:
  whether RAN4 will specify power class 2 along with class 3 for DB-DC-HSUPA band combinations I+VIII, I+V, and II+V
  In case an additional power class is defined, UE can select the preferred power class and signal it to the network using the existing capability signaling similar to Rel-99, SC-HSUPA, and DC-HSUPA