## Slide 1: PCell Mandatory Support for FDD-TDD & Class A2
KDDI Corporation
3GPP TSG-RAN WG4 #76
Beijing, China, 24 – 28 Aug, 2015
Agenda Item: 5.1.4
Document for: Approval
R4-154263

## Slide 2: Background
PCell Mandatory Support discussion has been ongoing and gradually begun to show good progress.
This contribution tries to make further progress on FDD-TDD and Class A2 combinations.

## Slide 3: FDD-TDD CA
RP-150841 [1] was submitted in RAN#68. Although we still prefer that all bands shall become mandatorily PCell, interpretation of TS36.331 in [1] seems to be appropriate.
[Compromise Recommendation] For FDD-TDD CA, PCell support should be based on UE capability ”tdd-FDD-CA-PCellDuplex-r12”.
 PCell Mandatory support in all bands is unrealistic.
[Observation] For FDD-FDD CA or TDD-TDD CA, there is no
UE capability for indicating PCell support.
 Further discussion is needed. This contribution focuses Class A2 combinations.

## Slide 4: Class A2 Combinations
For Class A2 combinations, MSD requirements are specified in Table 7.3.1A-0a of TS36.101.
If there are UEs which do not support PCell in lower band, MSD requirements are not supported by them.
   This will cause UE fragmentation issue.

## Slide 5: Observation & Proposal
[Observation] For Class A2 combinations, PCell mandatory support in lower band is essential for avoiding UE fragmentation issue. This applies FDD-TDD CA as well.
[Proposal] For the UE which supports CA configuration in Table 7.3.1A-0a of TS36.101, the UE shall support PCell operation at least in lower band. For Higher band, further discussion might be needed.