## Slide 1: Lower Band 65 A-MPR Proposal for Japan
KDDI Corporation
3GPP TSG-RAN WG4 #76
Beijing, China, 24 – 28 Aug, 2015
Agenda Item: 9.1
Document for: Approval
R4-155312
<Revision of R4-154210>

## Slide 2: Background
B65 Simulation results for PHS protection have been provided from multiple companies;
  [1] R4-153140 from Nokia Networks
  [2] R4-154936 from Ericsson
  [3] R4-155044 from Qualcomm
  [4] R4-155101 from LG Electronic
This contribution makes two proposals based on simulation results above.

## Slide 3: Proposal#1
For component carrier which is confined within 1940 – 1980 MHz, below aspects should be approved.
  A-MPR is NOT needed to satisfy PHS protection requirement for 5MHz/10MHz/15MHz.
  20MHz CBW case will be confirmed in RAN4#76-bis.

## Slide 4: Proposal#2
For component carrier which is confined within 1920 – 1940 MHz, RAN4 should fix below “X”, “Y” and “Z” until RAN4#77.
NS value for Lower Band 65 of 20 MHz channel bandwidth with fc = 1930 MHz |  |  |  |  |  | 
RBstart | 0 – 23 | 24 – 75 |  |  | 76 – 99 | 
LCRB | ≥1 | ≤24 | 25 ~ X | (X+1) ~ 50 | 1 ~ (Z-1) | Z ~ 24
A-MPR [dB] | ≤11 | 0 | ≤[3] | ≤Y | ≤TBD | 0
NS value for Lower Band 65 of 15 MHz channel bandwidth with fc = 1932.5 MHz |  |  |  |  |  | 
RBstart | 0 – 7 | 8 – 66 |  |  | 67 – 74 | 
LCRB | ≥1 | ≤30 | 31 ~ X | (X+1) ~ 57 | 1 ~ (Z-1) | Z ~ 8
A-MPR [dB] | ≤11 | 0 | ≤[3] | ≤Y | ≤TBD | 0

## Slide 5: Clarification on Proposal#2  20MHz CBW case
NS value for Lower Band 65 of 20 MHz channel bandwidth with fc = 1930 MHz |  |  |  |  |  | 
RBstart | 0 – 23 | 24 – 75 |  |  | 76 – 99 | 
LCRB | ≥1 | ≤24 | 25 ~ X | (X+1) ~ 50 | 1 ~ (Z-1) | Z ~ 24
A-MPR [dB] | ≤11 | 0 | ≤[3] | ≤Y | ≤TBD | 0
RAN4 is asked to fix “X” where [3] dB A-MPR is required.
RAN4 is asked to fix “Y” where LCRB is 50. Note that RB#24 and RB#75 are used as PUCCH so LCRB = 50 is maximum.
RAN4 is asked to fix “Z” where no A-MPR is required.

## Slide 6: Clarification on Proposal#2  15MHz CBW case
RAN4 is asked to fix “X” where [3] dB A-MPR is required.
RAN4 is asked to fix “Y” where LCRB is 57. Note that RB#8 and RB#66 are used as PUCCH so LCRB = 57 is maximum.
RAN4 is asked to fix “Z” where no A-MPR is required.
NS value for Lower Band 65 of 15 MHz channel bandwidth with fc = 1932.5 MHz |  |  |  |  |  | 
RBstart | 0 – 7 | 8 – 66 |  |  | 67 – 74 | 
LCRB | ≥1 | ≤30 | 31 ~ X | (X+1) ~ 57 | 1 ~ (Z-1) | Z ~ 8
A-MPR [dB] | ≤11 | 0 | ≤[3] | ≤Y | ≤TBD | 0