## Slide 1: Way forward for maximum power of the new power class for MTC
Ericsson, NTT DOCOMO INC., Sony, Verizon, Qualcomm, Nokia networks, Huawei, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Gemalto, Sequans, Intel
3GPP TSG-RAN WG4 Meeting #76 R4-155348
Beijing, China, Aug 24-28, 2015

## Slide 2: Background
In RAN4#75, it was agreed that the maximum transmit power for the new UE power class is not less than 20dBm
RAN4 was to investigate until this meeting to agree on the exact achievable maximum UE power while considering:
  Cost for an integrated (monolithic) MTC system; i.e. transceiver, PA, baseband and application processor
  UE supports more than one frequency band.
  Impact of frequency dependency, half duplex and full duplex aspect
  Impact on average energy consumption
    When operating in normal coverage
    When operating in extended coverage
  Note: RAN4 is not required to study impact of the maximum power of the new UE power class on system capacity.
The new UE power class will be applicable to MTC UEs only, i.e. a new table for UE Power Class of MTC UE will be defined in section 6.2.2 of TS 36.101

## Slide 3: WF on maximum transmit power for the new UE power class
The maximum transmit power for the new UE power class is 20dBm.
For Rel-13 LC MTC UE both the new power class and the normal UE power 23dBm are valid.