## Slide 1: 3GPP TSG-RAN WG4 Meeting #76BIS R4-155586 Sophia Antipolis, France, October 12 – 16, 2015 Agenda item: 5.7 Source: Intel Corporation Title: Summary of the FCC rules in the 3.5GHz band Document for: Discussion
Summary of the FCC rules in the 3.5GHz band

## Slide 2: USA 3.5GHz Band
FCC released R&O on 04/21/2015 [1].
SI proposal on the USA 3.5GHz band for LTE was postponed to December 2015 [2].
3550 – 3700 MHz (total 150MHz spectrum)
Within the 3GPP Bands 42/43

## Slide 3: SAS Framework (1/2)
Three tiers system (incumbents, PAL, and GAA)
Incumbent Access Users
  1st tier 3550-3700MHz and below 3550MHz
  Ground-based and ship borne federal radar systems, fixed satellite services and grandfathered commercial users in the 3650-3700 MHz segment
Citizen Broadband Radio Service (CBRS, 3550-3700MHz)
  Priority Access Licensees (PAL), 2nd tier 3550-3650MHz
  General Authorized Access (GAA), 3rd tier 3550-3700MHz, protecting 2nd tier
  CBRS devices will be assigned frequencies dynamically by a Spectrum Access System (SAS).
  Equipped with Environment Sensing Capabilities (ESCs) to detect federal frequency usage in and adjacent to the 3.5GHz band
All CBRS users must protect the incumbent tier (1st tier) of users in the band.

## Slide 4: SAS Framework (2/2)
  Apportionment between PAL and GAA
  Maximum of 70 MHz may be reserved for PALs in any given license area at any time (0-70MHz).
  The remainder of the available frequencies should be made available for GAA usage (80-150MHz).
  Priority Access Licensees (PAL), 2nd tier
  Operate over 10MHz unpaired channels, 3-year license
  Dynamically assigned by SAS
  Max 40MHz (out of 70MHz) contiguous channels in one census tract at one time
General Authorized Access (GAA), 3rd tier
  Have to protect the 1st and 2nd tier users
  Have no expectation of interference protection from the 1st and 2nd tier users
  No explicit limit on GAA spectrum aggregation

## Slide 5: FCC Rules for PAL and GAA
  Regulated under new Part 96 of the FCC rules
  FCC rules use the emission limits, exclusion and protection zones enforced by SAS and ESC to protect the incumbents (1st tier).
  Same technical rules for PAL and GAA
  PAL requires license to operate
  GAA operates under a licensed-by-rule framework
  BS and UE must be capable of two-way operation, but not required to operate in a two-way mode.

## Slide 6: BS (CBSD) TX Power (1/2)

## Slide 7: BS (CBSD) TX Power (2/2)
Within 60 seconds after the ESC communicates that it has detected a signal from a federal system in a given area, the SAS must either confirm suspension of the CBSD’s operation or its relocation to another unoccupied frequency.
A CBSD must cease transmission, move to another frequency range, or change its power level within 60 seconds as instructed by an SAS.
CBSD shall protect existing FSS Earth Stations in 3600-3650MHz and 3700-4200MHz.

## Slide 8: UE (End User Device) TX Power
UE must be authorized and controlled by an SAS-authorized CBSD.
EIRP of 23dBm per 10MHz channel, with power control
UE must discontinue operation, change frequency, or power level within 10 seconds of receiving instruction for its CBSD.

## Slide 9: Received Signal Strength Limits
For both PAL and GAA users, CBSD transmissions must be managed such that the aggregate received signal strength shall not exceed -80dBm/10MHz at the service area boundary of any co-channel PAL. Measured at 1.5m height.
Not apply to the boundary if operated by the same PAL.

## Slide 10: BS (CBSD) and UE Emission Limits
-13 dBm/MHz from 0 to 10 MHz from the SAS assigned channel edge
-25 dBm/MHz beyond 10 MHz from the SAS assigned channel edge down to 3530 MHz and up to 3720 MHz
-40 dBm/MHz below 3530 MHz and above 3720 MHz
Measured when at max EIRP. 1MHz or 1% of BW within the first 1MHz offset.

## Slide 11: Reception Limits
PAL must accept adjacent channel and in-band blocking interference up to -40dBm/10MHz.

## Slide 12: Exclusion Zones
For Category A CBSDs, exclusion zones shall be maintained along the coastline shown at ntia.doc.gov/category/3550-3650-mhz. Exclusion zones shall also be maintained around federal radiolocation sites as set forth at ntia.doc.gov/category/3550-3650-mhz.
For Category B CBSDS, base and fixed stations may not be located within 80km of the following Federal Government radiolocation facilities (3650-3700MHz)
Some examples:

## Slide 13: Discussions
Re-use B42/B43 bands with minor changes in the spec
  FCC OOBE of -40dBm/MHz with 20 MHz offset is tighter than the B42/B43 -40dBm/MHz with 25/30 MHz offset. -40dBm/MHz can be solved by a new NS value (with higher A-MPR) if FCC accepts NS signaling, otherwise, RB restrictions for the lowest 10MHz carrier at the band edge are required.
Single filter implementation in B42/B43 can be used for 3550-3700 MHz.
CA can be solved with standard CA specifications.
  Intra-band contiguous CA (specific inter-band CA in B42/43)
There is no issue in channel arrangement.
  A new note to Table 5.7.3-1 in 36.101 to keep the channel numbers at the upper edge of B42 and the channel numbers at the lower edge of B43.
Re-use of existing bands leads to better eco-system. Defining a new band will delay the development of UE and increase testing effort.

## Slide 14: References
[1] FCC 15-47 (GN Docket No. 12-354), “Amendment of the Commission’s Rules with Regard to Commercial Operations in the 3550-3650 MHz Band”
[2] R4-151622, “New Study Item Proposal: US 3.5 GHz Band for LTE”, Verizon, and Qualcomm