## Slide 1: NS Versioning for DTV protection in Japan
KDDI Corporation
3GPP TSG-RAN WG4 #76-bis
Sophia Antipolice, France, 12 – 16 October, 2015
Agenda Item: 5.1
Document for: Approval
R4-155824

## Slide 2: Background
When introduction of CA_18A-28A had been discussed, it was approved that frequency range of Band 28 shall be limited from UL/DL = 703 – 748/758 – 803 MHz into 703 – 733/758 – 788 MHz (= only implement lower filter of Band 28 and not implement upper filter).
However, lower Band 28 filter cannot provide enough rejection to satisfy DTV co-existence requirement in Japan. Hence, PUCCH overprovisioning was introduced in Table 6.6.3.2-1 of TS36.101 from Rel-12.

## Slide 3: Current Specification in TS36.101
As one can see, RB limitation has been specified. In this case, 2RBs * 2 = 4RBs cannot be operated in Japan.
E-UTRA Band | Spurious emission |  |  |  |  |  | 
 | Protected band | Frequency range (MHz) |  |  | Maximum Level (dBm) | MBW (MHz) | NOTE
28 | E-UTRA Band 1, 4, 10, 22, 42, 43 | FDL_low | - | FDL_high | -50 | 1 | 2
 | E-UTRA Band 1 | FDL_low | - | FDL_high | -50 | 1 | 19, 25
 | E-UTRA Band 2, 3, 5, 7, 8, 18, 19, 20, 25, 26, 27, 31, 34, 38, 40, 41 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 11, 21 | FDL_low | - | FDL_high | -50 | 1 | 19, 24
 | Frequency range | 470 | - | 694 | -42 | 8 | 15, 35
 | Frequency range | 470 | - | 710 | -26.2 | 6 | 34
 | Frequency range | 662 | - | 694 | -26.2 | 6 | 15
 | Frequency range | 758 | - | 773 | -32 | 1 | 15
 | Frequency range | 773 | - | 803 | -50 | 1 | 
 | Frequency range | 1839.9 | - | 1879.9 | -50 | 1 | 
 | Frequency range | 1884.5 | - | 1915.7 | -41 | 0.3 | 8, 19
NOTE 34: This requirement is applicable for 5 and 10 MHz E-UTRA channel bandwidth allocated within 718-728MHz. For carriers of 10 MHz bandwidth, this requirement applies for an uplink transmission bandwidth less than or equal to 30 RB with RBstart > 1 and RBstart<48. |  |  |  |  |  |  | 

## Slide 4: Discussion
Even if 4RBs might be small number for certain companies, UL resource is quite important.
We would like to utilize this blank region by applying A-MPR. This can be achieved by NS versioning.
  NS_17 modification is necessary.

## Slide 5: Proposal
Modification of NS_17 should be approved from Rel-12 or Rel-13.
If above proposal is approved, multiple vendors are requested to provide simulation results to achieve DTV protection requirement in Japan by using lower filter of Band 28.

## Slide 6: Appendix
Current requirement is above. Two limitations below should be excluded by introducing A-MPR in NS_17.
  Limitation#1: 4RBs cannot be utilized.
  Limitation#2: Upper limit of RB allocation (=30) should be removed