## Slide 1: Band 18/Band 26 data
KDDI Corporation
3GPP TSG-RAN WG4 #76-bis
Sophia Antipolice, France, 12 – 16 October, 2015
Agenda Item: 7.1.2
Document for: Approval
R4-155860

## Slide 2: Background
How to specify TRP/TRS requirements in RAN4 has been discussed intensively.
As a result, it seems that measurement data on commercial products would be used for standardizing requirements for each band.
This contribution provides TRP/TRS data of Band 18/Band 26 commercial products and proposes requirements for these bands.

## Slide 3: Raw data
TRP (dBm) | 
B18 | B26
11.04 | 10.06
12.50 | 10.71
12.02 | 11.18
11.92 | 10.80
12.78 | 11.08
TRS (dBm) | 
B18 | B26
-83.42 | -82.30
-88.03 | -86.02
-85.81 | -84.33
-85.75 | -84.29
-87.20 | -86.04
Raw data for Band 18/Band 26 are available below.
So far, five samples are available. We understand the number of data is not enough to standardize RAN4 requirements.

## Slide 4: CDF

## Slide 5: Proposal
Although we understand the number of data is enough, our proposals for Band 18/Band 26 requirements are below based on current measurement data.
We will input more data in the next meeting to verify below proposals.
E-UTRA bands | TRP (dBm) | TRS (dBm)
Band 18 | 11.0 | -83.0
Band 26 | 10.0 | -83.0