## Slide 1: Wayforward on subframe offset reporting for DC enhancement
Intel, Ericsson, NTT DOCOMO, CATT
R4-156639
3GPP TSG-RAN WG4 #76
Sophia Antipolis, France, 12-16 October, 2015
Agenda Item: 7.9.3.1

## Slide 2: Way forward on subframe offset report mapping
Subframe boundary offset (Z) between MeNB and SeNB (Z) can be reported by UE
  The reporting range of absolute value of Z is between [700Ts, 1320Ts] with reporting granularity of 10Ts.
Table 1: UE Subframe boundary offset (Z) measurement report mapping
Reported Value | Measured Quantity Value | Unit
Z_00 | abs(Z) ≤ 700 | Ts
Z_01 | 700 < abs(Z) ≤ 710 | Ts
Z_02 | 710 < abs(Z) ≤720 | Ts
… | … | …
Z_61 | 1300 < abs(Z)  1310 | Ts
Z_62 | 1310 < abs(Z)  1320 | Ts
Z_63 | 1320< abs(Z) | Ts