## Slide 1: Way forward on SSTD measurement accuracy
Ericsson, Intel
3GPP TSG-RAN WG4 Meeting #76bis R4-156640
Sophia Anti-Polis, France, 12 – 16 October, 2015

## Slide 2: Background
SFN and Subframe Timing Difference (SSTD) measurement has three parts
  SFN offset measurement
  Frame boundary offset measurement
  Subframe timing boundary offset
The accuracy requirements in the next slide only corresponds to subframe timing boundary offset measurement.

## Slide 3: Way forward
Subframe timing boundary offset accuracy requirements are to be based on existing timing accuracy requirements for initial transmission, where for the neighbour cell/PSCell a DL system bandwidth of 1.4 MHz shall be assumed.
Subframe timing boundary offset accuracy requirements are to take into account tolerances both for PCell and the neighbour cell/PSCell, as well as the bandwidth of the PCell.
The UE requirements on accuracy of estimated Subframe timing boundary offset between PCell and a candidate PSCell shall depend on the bandwidth of the PCell (reference cell), e.g.
  ±48Ts (±1.6µs) when the DL system bandwidth of the PCell is 1.4 MHz, and
  ±36Ts (±1.2µs) when the DL system bandwidth of the PCell is 3 MHz or wider.
The requirements on accuracy of estimated Subframe timing boundary offset is to be applicable under the side condition Ês/Iot ≥ -3dB.