## Slide 1: Way forward on eD2D : General aspect and TX requirements
LG Electronics, Qualcomm Inc., Ericsson
3GPP TSG-RAN WG4 Meeting #76BIS R4-156858
Sophia Antipolis, France, 12 – 16 October, 2015

## Slide 2: Background
It has been agreed that, eD2D for MCC (Multiple Component Carrier) operation should be completed in Rel-13 time frame.
RAN4 already agreed two example band combinations for WAN-D2D operation as follow,
      B2(D2D)+B4(WAN)
      B28(D2D)+B1(WAN)

## Slide 3: General aspects
For the operating bands supported for simultaneous D2D-WAN transmissions the following ProSe/E-UTRA combinations apply.
For E-UTRA WAN CA operation the uplink is assigned to one E-UTRA band
E‑UTRA ProSe Band | E‑UTRA operating Band/E-UTRA CA operating Band
2 | 4
 | CA_2-4
28 | 1
 | CA_1-28

## Slide 4: TX requirements
For Rel-13 eD2D simultaneous WAN-D2D on separate bands, dual uplink inter-band CA TX requirements shall be reused.
  The transmit requirements for E-UTRA shall apply for the transmissions on E-UTRA carrier
  The transmit requirements for Rel-12 ProSe shall apply for the transmissions on ProSe carrier
TProSe (as agreed in Rel-12) should also be addressed in the Pcmax equations for legacy CA.

## Slide 5: References
[1] R4-156116, “General Tx/Rx requirements for D2D-WAN simultaneous transmission,” Source: LG Electronics
[2]R4-155869, “D2D UE RF Requirements for Multiple Carriers,” Source: Ericsson
[3] R4-155553, “eD2D RF: Tx requirements,” Source: Qualcomm, Inc.