## Slide 1: Way Forward on Dual Connectivity measurement enhancements
Nokia Networks, Ericsson
R4-156871
3GPP TSG-RAN WG4 Meeting #76bis
Sophia Antipolis, France, 12-16 October, 2015
Agenda Item: 7.9.3.2

## Slide 2: Discussion
Background:
  WI on Dual Connectivity enhancements was agreed in [1], and includes one part covering:
    Enhancement of intra-frequency/inter-frequency/inter-RAT measurement requirements in DRX (RAN4)
[1] RP-150490, Dual Connectivity enhancements for LTE, NTT DOCOMO, INC.

## Slide 3: Discussion
Rel-12 RRM measurement core requirements for DC are that CG measurement requirements are based on the intra-frequency measurement requirements of the CG.
  For DC this means that there can be situations where the measurement delay of measurements performed by the UE in the two CGs is different due to the state of the DRX in the CGs.

## Slide 4: Discussion
Intra-frequency, inter-frequency and inter-RAT measurement proposal under discussion is as follows:
  If in DRX in PCell, measurement frequency is increased when the UE is scheduled in PSCell.
  PSCell measurement requirements would be unaffected by the PCell scheduling.
Applying above is under network control
  Single bit enables intra Pcell, interfrequency and interRAT measurements to follow SCG DRX state

## Slide 5: Way Forward
Interested companies are expected to bring pros and cons for next meeting.
RAN4 needs to make decision in RAN4#77 in order to be able to send LS to RAN2.