## Slide 1: Way Forward on how to handle harmonic mixing in RAN4
KDDI Corporation
3GPP TSG-RAN WG4 #76-bis
Sophia Antipolis, France, 12 – 16 October, 2015
Agenda Item: 5.1.2
Document for: Approval
R4-156899

## Slide 2: Background
How to handle harmonic mixing issue has been discussed almost for one year but there is no agreement in RAN4.
So far RAN4 identified the following carrier aggregations have the low band mixing problem.
  CA_26A-41A
  CA_28A-40A
  CA_20A-40A

## Slide 3: Possible Options
# | Handling of TS | Comments
Option 1 | Keep current spec.  No MSD due to HMI. | Implementation is limited. Certain L/O will not be allowed.
Option 2 | No MSD but add note into TS. | Allow flexible Implementation.  Note will be “RAN5 can skip MSD tests due to HMI”.
Option 3 | Specify MSD due to HMI into TS and RAN5 performs MSD tests. | MSD will be large (~40 dB). It seems meaningless to capture so large MSD into TS.
* HMI: Harmonic Mixing Issue

## Slide 4: Way Forward
KDDI proposes to approve Option 2.
How to choose L/O is depending on vendors’ policy and is clearly out of scope of 3GPP.
On the other hand, 3GPP specification should not impose single type of implementation.
MSD would be too large. It may not be beneficial to capture into TS and be tested.