## Slide 1: Way forward for rel-13 eMTC REFSENS
Sony, Ericsson, …
3GPP TSG-RAN WG4 Meeting #76bis
Sophia Antipolis, France, 12-16 October 2015
R4-156923

## Slide 2: Background
The work item “Further LTE Physical Layer Enhancements for MTC” was approved in RAN#67 [1]. In RAN4#76 it was agreed that requirements should be specified for the following bands [1]
Bands 1,2, 3, 4, 5, 7, 8, 12, 13, 18, 19, 20, 21, 26, 27, 28, 31, 39, 41 for normal operation
Bands 1, 2, 3, 4, 5, 7, 8, 12, 13, 18, 19, 20, 21, 26, 27, 28, 31 for half duplex FDD operation.
Rel-13 MTC may work in normal coverage mode or extended coverage mode.

## Slide 3: Way forward
The REFSENS value for rel-13 eMTC shall be based on an RX bandwidth corresponding to 6RB (i.e. 1.4MHz) for all applicable system bandwidths.
Re-use 2.5dB REFSENS relaxation for FDD and TDD, due to single RX, for rel-13 eMTC (same as rel-12).
REFSENS requirement for normal coverage mode applies to enhanced coverage mode.
The impact of 20dBm power class need to be further investigated.
Re-use the 1.7dB relaxation due to single RX for HD-FDD used in rel-12 for bands defined for 1.4MHz BW.
For bands not defined for 1.4MHz BW calculate REFSENS from 5MHz value -3.5dB (HD-FDD case).
The condition where UL resource blocks and DL resource blocks are located as close as possible but confined within the transmission bandwidth configuration for the channel bandwidth for UL and DL, respectively need to be investigated further.
Include B11 in rel-13 eMTC

## Slide 4: Reference
[1] RP-150492 “Revised WI: Further LTE Physical Layer Enhancements for MTC”
[2] R4-154862, “Proposal on MTC Bands for Further LTE Physical Layer Enhancements”
[3] R4-156240 “UE RF requirements for Rel-MTC”, NTT DOCOMO, INC
[4] R4-156252 “UE REFSENS for Rel-13 MTC in normal coverage mode”, Ericsson
[5] R4-156247 “Way forward for rel-13 eMTC REFSENS”, Sony
[6] R4-156253 “UE REFSENS for Rel-13 MTC in enhanced coverage mode”, Ericsson