## Slide 1: NS Versioning for DTV protection in Japan
KDDI Corporation
3GPP TSG-RAN WG4 meeting #77
Anaheim, CA, US, 16 – 20 November, 2015
Agenda Item: 7.53
Document for: Approval
R4-157044

## Slide 2: Background
When introduction of CA_18A-28A had been discussed, it was approved that frequency range of Band 28 shall be limited from UL/DL = 703 – 748/758 – 803 MHz into 703 – 733/758 – 788 MHz (= only implement lower filter of Band 28 and not implement upper filter).
However, lower Band 28 filter cannot provide enough rejection to satisfy DTV co-existence requirement in Japan. Hence, PUCCH overprovisioning was introduced in Table 6.6.3.2-1 of TS36.101 from Rel-12.

## Slide 3: Current Specification in TS36.101
As one can see, RB limitation has been specified. In this case, 2RBs * 2 = 4RBs cannot be operated in Japan.
E-UTRA Band | Spurious emission |  |  |  |  |  | 
 | Protected band | Frequency range (MHz) |  |  | Maximum Level (dBm) | MBW (MHz) | NOTE
28 | E-UTRA Band 1, 4, 10, 22, 42, 43 | FDL_low | - | FDL_high | -50 | 1 | 2
 | E-UTRA Band 1 | FDL_low | - | FDL_high | -50 | 1 | 19, 25
 | E-UTRA Band 2, 3, 5, 7, 8, 18, 19, 20, 25, 26, 27, 31, 34, 38, 40, 41 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 11, 21 | FDL_low | - | FDL_high | -50 | 1 | 19, 24
 | Frequency range | 470 | - | 694 | -42 | 8 | 15, 35
 | Frequency range | 470 | - | 710 | -26.2 | 6 | 34
 | Frequency range | 662 | - | 694 | -26.2 | 6 | 15
 | Frequency range | 758 | - | 773 | -32 | 1 | 15
 | Frequency range | 773 | - | 803 | -50 | 1 | 
 | Frequency range | 1839.9 | - | 1879.9 | -50 | 1 | 
 | Frequency range | 1884.5 | - | 1915.7 | -41 | 0.3 | 8, 19
NOTE 34: This requirement is applicable for 5 and 10 MHz E-UTRA channel bandwidth allocated within 718-728MHz. For carriers of 10 MHz bandwidth, this requirement applies for an uplink transmission bandwidth less than or equal to 30 RB with RBstart > 1 and RBstart<48. |  |  |  |  |  |  | 

## Slide 4: Discussion
Even if 4RBs might be small number for certain companies, UL resource is quite important.
We would like to utilize this blank region by applying A-MPR. This can be achieved by NS versioning.
  NS_17 modification is necessary.

## Slide 5: Proposal
Modification of NS_17 should be approved from Rel-13. (Unlikely with NS_05 modification, it would be impossible to modify from Rel-12 because we do not have A-MPR simulation results so far.)
If above proposal is approved, multiple vendors are requested to provide simulation results to achieve DTV protection requirement in Japan by using lower filter of Band 28.

## Slide 6: Appendix
Current requirement is above. Two limitations below should be excluded by introducing A-MPR in NS_17.
  Limitation#1: 4RBs cannot be utilized.
  Limitation#2: Upper limit of RB allocation (=30) should be removed