## Slide 1: Way Forward on MSD for CA_28A-42A
KDDI Corporation
3GPP TSG-RAN WG4 meeting #77
Anaheim, CA, US, 16 – 20 November, 2015
Agenda Item: 7.43.2.2
Document for: Approval
R4-157050

## Slide 2: Background
CA_28A-42A is classified as Class A2 because 5th harmonic of Band 28 UL will fall into Band 42 DL.
Thus, MSD requirements would be needed.
Also for delta values, RAN4 does not have same understanding. So way forward is needed.

## Slide 3: Reports Summary
Simulation results were provided from two companies. Above table summarizes them.
We can see large differences between two companies.
Assumption: Harmonic Trap Filter is included. | MSD (dB) |  |  | 
 | 5 MHz | 10 MHz | 15 MHz | 20 MHz
Mediatek (R4-155973) | 9.0 | 6.5 | 5.2 | 4.4
Qualcomm (R4-156520) | 16.6 | 13.7 | 12.0 | 10.9
Band 42 REFSENS | - 99 dBm | -96 dBm | -94.2 dBm | - 93 dBm
Observation#1: Large differences are found between results from two companies.

## Slide 4: Simulation Assumptions
Almost similar assumptions are utilized but triplexer attenuation @ H5 shows 5 dB difference (20 dB in MTK and 15 dB in QC).
Assumed composite powers @ H5 are below;
  MTK: -84.5 dBm [(main:-87.3) + (div.: -87.8) dBm]
  QC: -88 dBm
Observation#2: MTK assumes higher interference than that of QC’s but MTK’s results indicate smaller MSD.

## Slide 5: Conclusion
Results from two companies show different behavior. Namely, higher composite power @ H5 indicates smaller MSD results.
Therefore, we believe results from R4-155973 would be achievable when smaller composite power is assumed than -84.5 dBm.
As a result, MSD from R4-155973 can be approved (or more inputs are encouraged).
Proposal: MSD in 5973 should be approved

## Slide 6: Annex: Possible requirements
Channel bandwidth |  |  |  |  |  |  |  | 
EUTRA CA Configuration | EUTRA band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex mode
CA_28A-42A | 28 |  |  | -98.3 | -95.3 | -93.5 | -90.8 | FDD
 | 42 |  |  | -89.5 | -89 | -88.5 | -88.1 | 
Table 1: Assumed MSD due to 5th harmonic of Band 28 UL