## Slide 1: Way Forward on LTE TRP/TRS discussion
Source： NTT DOCOMO, INC.
Agenda Item: 7.1.1
Document for: Approval
R4-157423

## Slide 2: Background
In the past several meetings, UMTS TRP/TRS for BHH and LEE have been discussed.
LTE requirement and some types of device are remained without discussion. Below table is referred to GCF LS(R4-146601) extracting only high priority test item.
It is discussed align with agreed WF (R4-75AH-TRPS-0018), however, UMTS requirement is still discussed, and LTE does not yet.
Test Methods and Limits (both normative with pass/fail criteria and recommended) | RAT | Priority | Test Requirement | Situation in 3GPP
For handheld devices supporting voice and width < 72 mm | E-UTRA | 1 | Talk mode BHHR/L Browsing mode HR/L | Both are not discussed
For handheld devices supporting voice and width < 72 mm | UTRA | 1 | Talk mode BHHR/L Browsing mode HR/L | BHH is under discussion Browsing is not discussed
For data-centric devices | E-UTRA | 1 | Free Space measurements for Notebook LEE and Tablet LEE Free Space measurements (with ground plane phantom) for LME In addition, GCF requires RAN4 to develop a Test Specification or guideline for generic data centric devices, e.g.M2M device, SD Card Modem, etc. | UMTS: Notebook LEE is Fin.. Tablet LEE is under discussion. LME is not discussed. LTE: all of them are not discussed.
For data-centric devices | UTRA | 1 |  | 

## Slide 3: Way forward 1/3
  UMTS requirement (BHH, and Tablet) shall be finalized in RAN4#77. Discussion shall be shifted to LTE requirement.
For LTE TRP/TRS requirement, additional framework can be added.
Discussion shall be basically align with agreed WF (R4-75AH-TRPS-0018).
UMTS requirement is for Rel-13, and others should be shift to Rel-14.
OTA TRP/TRS requirements are defined as described below:

## Slide 4: Way forward 2/3
Additional framework for LTE requirement is as follows
  LTE value shall be defined derived from OTA results not UMTS requirement.
  To promote discussion smoothly, deadline shall be defined with regard to submit measurement results.
  RAN4 CDF shall not be accounted by one company results.
    Option 1 : Defining limitation: One company can provide the [40] test results maximum.
    Option 2 : No limitation but, data is eliminated if a company provide larger number of results exceeding the 50% of RAN4 CDF.
      If an operator provides larger number, better data of the operator is eliminated. #1
      If a vender provides larger number, worse data of the vender is eliminated. #1
    Option 3 : Align number of results in RAN4 CDF between vender (50%) and operator (50%).
      If operators provide larger number, better data of operators is eliminated. #1
      If venders provide larger number, worse data of venders is eliminated. #1
    Option 4: All company CDF's are having equal weight when RAN4 CDF is calculated. But, one company need to provide more than [10] results per band.
    #1 Note: Because operators tend to provide better results, and venders tend to provide worse results, it should be taken account when data is eliminated.
OTA TRP/TRS requirements are defined as described below:

## Slide 5: Way forward 3/3
  For specific band, there are less results. Specify how to handle such bands.
    The data shall be provided at least 15 per band.
    Option 1: It can be merged with other bands which are closer frequency. (e.g. for band 13, band 12, 14, 17, 28). These bands are defined with same requirement.
    Option 2: Define based on the results of each band. However, the results may be tuned for operating band, it should be taken account. (e.g. 20/80% value are defined as Recommended value)
  For TRP, the minimum of the minimum requirement is align with the UMTS delta between minimum of the minimum and avg. requirement.
  For TRS, the maximum of the minimum requirement is align with the UMTS delta between maximum of the minimum and avg. requirement.
OTA TRP/TRS requirements are defined as described below: