## Slide 1: WF on DL Control Channel IM Interference models
Intel Corporation, ZTE, Ericsson, LGE, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #77 Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.4
R4-158135

## Slide 2: Way Forward (1)
Interference power profile
  Rel-12 NAICS WI for Scenario 1, Low SINR, 40% RU
  Option 1: High INR (I1/Noc = 13.91 dB, I2/Noc = 3.34 dB)
  Option 2: Medium INR (I1/Noc = 7.77 dB, I2/Noc = 2.29 dB)
Interference CRS pattern
  Colliding CRS Cell IDs pattern: Cell ID 0/6/1 (S/I1/I2)
  Non-Colliding CRS Cell IDs pattern: Cell ID 0/1/6 (S/I1/I2)
  May be further revisited in case technical issues are identified
Antenna configuration and number of CRS APs
  2x2 antenna configuration with low correlation, 2 CRS APs

## Slide 3: Way Forward (2)
PDCCH/PDCCH/PHICH interference model for synchronous networks
  The following serving and interference cell CFI values are used
    Option 1: CFIS = 1, CFII = 1
    Option 2: CFIS = 3, CFII = 3
    Option 3: CFIS = 3, CFII = 1
  PDCCH interference is emulated using random QPSK-modulated symbols with the SFBC-based precoding.
  Working assumption: PHICH interference is emulated using random QPSK-modulated symbols with the SFBC-based precoding.
    Companies can bring inputs on the explicit PHICH interference model in the next meeting.
  Partial PDCCH/PHICH interference loading is used. Loading level is FFS (e.g. 50 or 75%).
  Non-uniform PDCCH/PHICH power boosting is used. Details FFS (e.g. random value from -6 to 6 dB)
  Interference presence and power boosting modeling granularity is FFS between per-REG and per-CCE level.
  Time and frequency offset model: Reuse Rel-12 NAICS assumptions for performance gain test cases (i.e. Interference cell #1 – 2us, 200Hz, Interference cell #2 – 3us, 300Hz)
  Both colliding and non-colliding CRS scenarios are considered.

## Slide 4: Way Forward (3)
EPDCCH interference model for synchronous networks
  Control region duration in the serving and interference cells
    Previous agreements are revised to align with the existing EPDCCH FRCs
    Distributed EPDCCH: CFI=2, EPDCCH starting symbols is derived from CFI
    Localized EPDCCH: The EPDCCH starting symbol is 2. CFI = 1. EPDCCH starting symbol is RRC configured.
    Aligned control regions and EPDCCH starting symbols in the serving and interference cells
  Non-colliding CRS scenarios is considered only
  PDSCH interference model
    Interference structure
      Option 1: Reuse PDSCH interference model from Rel-11 Type A receiver requirements
      Option 2: TM9 QPSK RI = 1
    Partial loading model is used.
      Option 1: per-TTI level partial level model (i.e. on/off interference model)
      Option 2: per-PRB model
      Loading level is FFS (e.g. 50%)

## Slide 5: Way Forward (4)
Companies are encouraged to bring inputs on further downselection of the interference model parameters in the next meeting