## Slide 1: Way Forward on requirements for measurements for Rel-13 MTC UE
Ericsson, Nokia Networks, Alcatel-Lucent, Intel Corporation, […]
R4-158174
3GPP TSG RAN WG4 Meeting #77
Anaheim, US, November 16-20, 2015
Agenda Item: 7.7.5

## Slide 2: Background
RAN4 has studied measurement requirements performance for Rel-13 MTC for the last few meetings.
The progress from last meeting was captured in following WFs:
  R4-156655, “Way Forward on Gaps for eMTC measurement”
  R4-156657, “Way Forward on eMTC measurement requirements”
There were some remaining issues left as FFS, and this has been discussed at RAN4#77 meeting and is being captured in this document.

## Slide 3: Proposals for normal coverage
L1 measurement period:
  Rel-12 category 0 UE requirement on L1 measurement period (400 ms) for RSRP/RSRQ is reused for Rel-13 MTC UEs under normal coverage.
Cell detection delay:
  Rel-12 category 0 UE requirement on cell detection delay (600 ms for PCI acquisition + 400 ms measurement) is reused for Rel-13 MTC UEs under normal coverage.
From RAN4 perspective the legacy gap pattern is reused by Rel-13 MTC UEs for retuning to central PRBs dedicated for intra-frequency. This is subject to RAN1 LS reply.

## Slide 4: Proposal for enhanced coverage
L1 measurement period for RSRP/RSRQ is defined as 800 ms for Rel-13 MTC UEs under enhanced coverage.
Minimum SNR level to which the new accuracy requirements are applicable are changed from FFS to -15 dB.
Cell detection delay requirements is defined as follows for UEs operating under enhanced coverage
  Option 1: 320s detection time with 0.8s sampling period with the side condition below table
  Other options are not precluded:
From RAN4 perspective the, legacy gap pattern is reused by Rel-13 MTC UEs for retuning to central PRBs dedicated for intra-frequency. This is subject to RAN1 LS reply.
SI reading requirement
  Rel-12 category 0 UE requirements on CGI acquisition requirements of [190] ms is used.
  The exact repetition number for MIB/SIB1bis is pending RAN1 agreement.
  The requirement on minimum ACK/NACKs is TBD.
SCH Ês/Iot of already identified cell including serving cell: Q1 | Neighbouring cell SCH Ês/Iot: Q2 | Tbasic_identify_E-UTRA_FDD_UE cat M1, intra (s)
-15≤Q1<-6 | -15≤ Q2 < -6 | 320
-15≤Q1<-6 | Q2-6 | 320
Q1 -6 | Q2-6 | Requirements in 8.11.2 apply