## Slide 1: Way forward on how to apply ACLR and ACS on coexistence study for standalone case
Intel, Ericsson, Huawei, Nokia, Qualcomm
R4-158210

## Slide 2: how to apply ACLR and ACS on coexistence study for standalone case
First step for UL and DL
  Assume LTE ACLR is flat on the adjacent 10MHz channel
  Assume LTE ACS is flat on the adjacent 10MHz channel
  Assume NB-IoT ACLR is flat on the adjacent 10MHz
  Assume NB-IoT ACS is flat on the adjacent 10MHz
  Get simulation results
Second step for DL and [UL]
  Compute NB-IoT ACLR according to GSM mask
  Apply the GSM ACS to NB-IoT
  Get results from the first step, based on the calculated NB-IoT ACLR and ACS
  If the result is too pessimistic, go to step 3.
  If the result of NB-IoT performance is too optimistic, go to step 4.
Third step
  Need email discussion to find out more appropriate way to handle ACLR and ACS, and re-do simulations
Fourth step
  Need email discussion to find out more appropriate way to handle LTE ACLR, and re-do simulations