## Slide 1: WF on EIRP Accuracy
Alcatel-Lucent, Nokia, NEC, CATT, SEI, ZTE
3GPP RAN4#77 R4-158297
Anaheim, CA, USA, 16-20 Nov, 2015

## Slide 2: Contributed Data
Proposals | TRXU | Steering | Array | Value [dB]
CATT, R4-145627 | 2 | 0.5 | 1.2 | 2.4
NEC, R4-145901 | 2 | 1.5 | 1.5 | 2.9
Huawei, R4-146176 | 2 | 0.5 | 1 | 2.3
Ericsson, R4-146289 |  |  |  | 2.25
Nokia Networks, R4-153498 | 2 | 1.5 | 1.5 | 2.9
Vodafone, R4-75AH-AAS-0087 | 1 | 0.5 | 1 | 1.5
Telecom Italia, R4-146708 | 1 | 0.5 | 1 | 1.5
CMCC, R4-75AH-AAS-0005 | 1 | 0.5 | 1 | 1.5
Kathrein, R4-152625 | 1 | 0.5 | 1 | 1.5
Alcatel-Lucent, R4-156946 | 2 | 1 | 1 | 2.4
SEI | 2 | 1.5 | 1.5 | 2.9
Average (individual) | 1.6 | 0.85 | 1.17 | 2.16
Average (individual with TRXU at 2dB) | 2 | 0.85 | 1.17 | 2.47

## Slide 3: Background
Error model consisting of: transceiver accuracy, steering error and array error. Agreed methodology is to sum through Root sum square of the three error sources.
Averages are 2.16 dB (with 1.6 dB transceiver accuracy) and 2.47 dB (with 2 dB transceiver accuracy). Delta is largest, up to 1 dB, in transceiver accuracy and steering error.

## Slide 4: Proposal
Based on previously approved 2 dB transceiver accuracy, the proposal is:
  Accuracy of declared EIRP of 2.4 dB.