## Slide 1: WF on candidate advanced receivers for Control Channel IM
Huawei, Hisilicon, xx, …
3GPP TSG-RAN WG4 Meeting #77 Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.4
R4-158383

## Slide 2: Background
The Objectives in WID RP-151107 on candidate advanced receivers are:
In RAN4 76bis and RAN4 77 meeting, there were different understandings on the to-be-specified candidate receiver(s) in this WID.
  For example: whether the MMSE-IRC only or CRS-IC only receiver would be specified for PCFICH/PDCCH or not?
The candidate advanced receivers to be considered for demodulation requirements are the existing PDSCH receiver structures defined in Rel-11/Rel-12, with capability of
  Linear suppression of control channel interference of interfering cells such as
    MMSE-IRC
    E-MMSE-IRC
And
  Cancellation of CRS interference of interfering cell
  ……
Specify requirements on demodulation of PCFICH/PDCCH with above identified advanced receivers
  ……

## Slide 3: Way forward
It’s confirmed that, based on WID RP-151107, RAN4 will specify requirements on demodulation of PCFICH/PDCCH/PHICH with following identified advanced receiver(s) :
  LMMSE-IRC + CRS-IC
  And/or
  E-LMMSE-IRC + CRS-IC
Whether specify the requirements of other receiver(s) for PCFICH/PDCCH/PHICH, such as LMMSE-IRC only receiver or CRS-IC only receiver, depends on feasibility study and RAN plenary’s decision.