## Slide 1: WF on MPR and A-MPR for UL 256QAM
Ericsson
3GPP TSG-RAN4 Meeting #80bis R4-167907
Ljubljana, Slovenia, 10-14 October, 2016

## Slide 2: Background
In RAN4#80 it was agreed that [R4-166953],
  Transmitter EVM requirement for UL256QAM should be 3.5%
  Companies will provide simulation results for MPR for single carrier in RAN4#80bis

## Slide 3: Way forward
Observation 1: MPR of contiguous allocation should be 3dB
Observation 2: It is proposed that the following formula is used for MPR of UL 256QAM non-contiguous allocation for licensed bands:
MPR = CEIL {MA, 0.5},
where MA is defined as follows
MA = 8.00-10.12A ; 0.00< A ≤ 0.33
4.66 ; 0.33< A ≤1.00
Observation 3: The MPR requirements for UL 256QAM in unlicensed bands will be handled under eLAA work item.