## Slide 1: WF on Enhanced CRS-IM Performance Requirements
Intel Corporation, Huawei, HiSilicon, LGE, Ericsson
3GPP TSG-RAN WG4 Meeting #80bis Ljubljana, Slovenia, 10 - 14 Oct., 2016
Agenda Item: 8.31
R4-168638

## Slide 2: Background
In RAN #73 meeting the WI on the LTE Enhanced CRS and SU-MIMO Interference Mitigation Performance Requirements was approved [RP-161877].
The following CRS-IM enhancements work objectives are captured in the WID:
  Stage 1: Investigate performance benefits and feasibility of using CRS-IM receivers:
  Stage 2: Specify UE demodulation and CSI reporting performance requirements to verify practical CRS-IM operation for the identified scenarios based on the outcome of Stage 1.
Stage 1 includes the following components:
  Identification of target scenarios
  Identification of reference CRS-IM receiver structure assumptions
  Evaluation of CRS-IM performance
This WF provides agreements on the target scenarios and reference receivers for the Stage 1 investigations of CRS-IM enhancements
Companies are encouraged to provide further inputs on the scenarios and reference receivers performance/complexity analysis in RAN4 #81
  In stage 2, test cases will be selected based on evaluation on performance gain, UE implementation complexity and test coverage

## Slide 3: Scenarios (1)
Further investigate CRS-IM enhancements for the scenarios in the table below:
  Companies are encouraged to bring further inputs on the scenarios prioritization
Scenario | Number CRS APs |  | # of UE RX chains | Description
 | Serv. Cell | Interf. Cell |  | 
Scenario #1 (2RX + 4/4 CRS) | 4 | 4 | 2 | 2 RX antennas UEs with 4 CRS APs in the serving and interference cells.
Scenario #2 (2RX + 2/4 CRS) | 2 | 4 | 2 | 2 RX antennas UEs with mix of 2/4 CRS APs in the serving and interference cells.
Scenario #3 (2RX + 4/2 CRS) | 4 | 2 | 2 | 2 RX antennas UEs with mix of 4/2 CRS APs in the serving and interference cells.
Scenario #4 (4RX + 2/2 CRS) | 2 | 2 | 4 | 4 RX antennas UEs with 2 CRS APs in the serving and interference cells.
Scenario #5 (4RX + 4/4 CRS) | 4 | 4 | 4 | 4 RX antennas UEs with 4 CRS APs in the serving and interference cells.
Scenario #6 (4RX + 2/4 CRS) | 4 | 2 | 4 | 4 RX antennas UEs with mix of 2/4 CRS APs in the serving and interference cells.
Scenario #7 (4RX + 4/2 CRS) | 2 | 4 | 4 | 4 RX antennas UEs with mix of 4/2 CRS APs in the serving and interference cells.

## Slide 4: Scenarios (2)
Physical channels
  PDSCH (first priority):
    TM4
    TM9
    TM10 is FFS
  DL control channels (second priority)
    PDCCH/PCFICH
    PHICH
    EPDCCH

## Slide 5: Scenarios (3)
CRS pattern scenarios
  First priority: Non-colliding CRS scenarios
  Second priority: Colliding CRS scenarios
Cell ID pattern
  PDSCH evaluations (S/I1/I2)
    Non-colliding CRS
      Option 1: 0/1/6
      Option 2: 0/1/128
    Colliding CRS: 0/6/1
  DL control channel evaluations (S/I1/I2)
    Non-colliding CRS: 0/1/6
    Colliding CRS: 0/6/1

## Slide 6: Scenarios (4)
Interference model for PDSCH
  Reuse Rel-13 CRS-IM interference model
    I1/Noc = [10.45]dB; I2/Noc = [4.6] dB; 20% RU
    Further discuss whether to consider other RUs and interference profiles based on CRS-IM TR 36.863
Interference model for DL Control Channels
  Interference power profile
    Option 1: Reuse Rel-13 CCIM interference power profiles. I1/Noc = 13.91 dB; I2/Noc = 3.34 dB.
    Option 2: Reuse Rel-13 CRS-IM interference power profiles. I1/Noc = 8.36 dB; I2/Noc = 1.66 dB (RU=50%, 50%-tile from 36.863)
    Other options are not precluded
  Interference model
    PDCCH/PCFICH/PHICH: Reuse Rel-13 CCIM control region interference model
    EPDCCH model is FFS
      Option 1: CRS-only interference model
      Option 2: Reuse PDSCH interference model

## Slide 7: Scenarios (5)
Antenna correlation models
  Low antenna correlation model
Number of TX antennas
  2 and 4 TX antennas
  DMRS based PDSCH TMs and EPDCCH: Limit analysis by 2 CRS APs
  CRS-based PDSCH TMs, PDCCH/PCFICH, PHICH: Number of CRS APs is same as number of eNB TX antennas
MCS
  Rank 1 16QAM ½
  Other MCS are not precluded

## Slide 8: Reference Receivers (1)
Baseline receivers
  PDSCH: LMMSE-IRC
  DL Control Channels: LMMSE-MRC (companies are also encourage to provide results for LMMSE-IRC)
Enhanced reference receiver structures
  PDSCH: LMMSE-IRC + CRS-IM
  DL Control Channels: Type A CCIM receiver (LMMSE-IRC + CRS-IM)
  Enhanced CRS-IM receivers
  Further investigate performance/complexity of Non-colliding CRS-IM for 4RX UEs.
  Further investigate Non-colliding CRS-IM for the scenarios with different number of APs in serving and interference cells
  Further study LMMSE-IRC and CRS-IM for Colliding CRS scenarios operation with second priority

## Slide 9: Reference Receivers (2)
  Enhanced CRS-IM receivers
    Further study the performance/complexity for the following non-colliding CRS-IM reference receivers for 4 CRS APs
      Receiver #1: Full complexity four ports CRS-IM processing
      Receiver #2: Reduced complexity CRS-IM processing
        Full complexity two ports + low complexity two ports (e.g. puncturing)
Number of cancelled interference cells
  Option 1: 1
  Option 2: 2
  Companies are encouraged to bring analysis on the performance/complexity and also 2nd interferer detection feasibility