## Slide 1: WF on Feasibility Test for Enhanced SU-MIMO
3GPP TSG-RAN WG4 Meeting #80bis Ljubljana, Slovenia, 10 - 14 Oct., 2016
Agenda Item: 8.31.3.1
R4-168639
LG Electronics, Intel, Huawei, HiSilicon, Ericsson

## Slide 2: Background
In RAN #73 meeting the WI on the LTE Enhanced CRS and SU-MIMO Interference Mitigation Performance Requirements was approved [RP-161877].
In the WID, to specify performance requirements for enhanced SU-MIMO
  RAN4 needs to investigate performance benefits and feasibility of using SU-MIMO IM receivers for the scenarios with 4 receive antennas UEs in Stage 1.
    Investigate and agree on target scenarios including layer number for spatial multiplexing, MCS, propagation conditions and others for performance evaluation
    Identify the reference receiver structure for SU-MIMO IM evaluation
    Evaluate the performance of enhanced SU-MIMO IM receivers
Companies are encouraged to provide further inputs on the scenarios and reference receivers performance/complexity analysis in RAN4 #81.

## Slide 3: Evaluation scenarios
MIMO Rank 2 scenarios with 4 Rx antenna
  Candidate scenarios for initial analysis
    Transmission mode
      TM4 with 2Tx and 4Tx
      TM9 with 2Tx and 4Tx
    Modulation order
      16QAM, 64QAM, 256QAM
  Other scenarios are not precluded and companies are encouraged to bring further inputs
    FFS if inter cell interference scenarios are considered
  For 256QAM scenarios, RAN4 will decide feasibility with following considerations as mentioned in WID
    operating SNR, realistic Tx EVM assumption, performance gains, reference receiver complexity and testability

## Slide 4: Evaluation scenarios
MIMO Rank 3/4 scenarios with 4 Rx antenna
  Candidate scenarios for initial analysis
    Transmission mode
      TM3 with rank 3
      TM4 with rank 4
      TM9 with rank 4
    Modulation order
      16QAM, 64QAM, 256QAM
  Other scenarios are not precluded and companies are encouraged to bring further inputs
    FFS if inter cell interference scenarios are considered
  For 3/4 layers and 256QAM scenarios, RAN4 will decide feasibility with following considerations as mentioned in WID
    operating SNR, realistic Tx EVM assumption, performance gains, reference receiver complexity and testability

## Slide 5: Evaluation scenarios
Antenna configuration
  ULA Medium correlation (α=0.3, β=0.9)
  ULA Medium A correlation (α=0.3, β=0.3874)
  Optional for 3/4 layers scenarios:
    XPOL Medium A correlation (α=0.3, β=0.6, γ=0.2)

## Slide 6: Receiver Structures
Baseline receiver
  LMMSE-IRC
Reference receiver for enhanced SU-MIMO IM
  R-ML
    WID: R-ML is considered in high priority
  CWIC is not precluded for performance evaluation