## Slide 1: WF on V2V demodulation performance tests
Huawei, HiSilicon, LGE, Qualcomm, Ericsson, Intel Corporation
3GPP TSG-RAN WG4 Meeting #80bis Ljubljana, Slovenia, 10 - 14 Oct., 2016
Agenda Item: 8.19.4
R4-168710

## Slide 2: Background
According to the time budget from RAN#73, the performance part for WI: “Support for V2V services based on LTE sidelink” should start from RAN4#80bis meeting
Contributions are submitted to identify new requirements in this meeting for LTE_SL_V2V-Perf
Some guidelines are needed for evaluations of next meeting

## Slide 3: Way Forward
Working assumptions
  Band47 for V2V performance requirements, i.e. standalone V2V operation will be defined in V2V and Performance requirements for non-standalone scenario will be defined in V2X.
  only consider GNSS or GNSS-equivalent as the synchronization source for V2V performance requirements
    TX/RX Timing error: ±12Ts
    TX/RX Frequency error: ±600Hz
  AGC settling time (not used for demodulation)
    Single symbol
  Baseline: adjacent RBs are allocated for SA and its associated PSSCH transmission in the same subframe

## Slide 4: Way Forward
Physical channels
  Introduce performance requirement for PSSCH and PSCCH
  Discuss whether PSSCH and PSCCH should be tested jointly
Test cases and purposes
  Single-link PSSCH and PSCCH demodulation performance
    Capability to handle high CFO
    Capability to handle high and low Doppler spread
    Capability of PSCCH DMRS blind detection
  Multi-link PSSCH and PSCCH demodulation performance
    Capability to perform simultaneous reception of multiple V2V links with different propagation conditions (time offset, carrier frequency error, delay spread, Doppler spread)
    Capability to perform reception of links with max power imbalance
  Maximum process test

## Slide 5: Way Forward
UE speed and propagation condition
  The maximum speed to be used for requirements is FFS
  Companies are encourage to provide evaluation results for different relative vehicular speeds and also LOS/NLOS conditions
    280km/h@5.9GHz,
    500 km/h@5.9GHz
    Other choice are not precluded
HARQ retransmission
  Should comply with RAN1/2 conclusion

## Slide 6: Reference V2V receiver
Reference V2V receiver assumptions
  RX timing window assumptions are FFS
    Option 1: set RX timing window on CP/2 from the GNSS reference time
    Other options not precluded
  Further study performance/complexity of CFO and Doppler shift algorithms
    Option 1: “cross-DMRS” estimation
    Option 2: “single-DMRS” estimation
  Further study channel and Doppler spread estimation impacts to the V2V UE demodulation performance.
  LMMSE-MRC reference receiver structure is used
  V2V UE receiver is capable of PSCCH DMRS cyclic shift blind detection

## Slide 7: For information
  Companies are encouraged to provide input on how to model these resource allocation in the demodulation test.