## Slide 1: Way forward on NB-IoT UE demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #80BIS
Ljubljana, Slovenia, 10-14, October, 2016
R4-168743

## Slide 2: NPDCCH demodulation requirements
The below is a summary of the proposed number of repetitions to satisfy 1% BLER in each case (Case 1&3 at SNR of -6dB, Case 2&4 at SNR of -12dB) from each contribution.
 | Case1 EPA5 2x1 low | Case2 ETU1 2x1 low | Case3 EPA5 1x1 | Case4 ETU1 1x1
RAN4#80 Assumption [R4-166656] | [64] | [512] | [128] | [512, 1024]
Ericsson[R4-168208] | 128 | 1024 | 128 | 1024
Intel[R4-167243] | 128 | 1024 | 128 | 1024
CATT[R4-167506] | 128 | 1024 | 128 | 1024
Huawei[R4-167568] | 64 | 512 | 128 | 1024
Qualcomm[R4-168040] | 64 | 512 | 128 | 1024
ZTE[R4-168157] | 64 | 512 | 128 | 512
Nokia[R4-168740] | 64 | 512 | 64 | 512
Samsung[R4-168148] | 64 | 512 | 128 | TBD

## Slide 3: NPDSCH demodulation requirements
The below is a summary of the proposed number of repetitions to satisfy 70% of Max throughput around the targeted SNR.
 | Case2 EPA5 2x1 low | Case3 ETU1 2x1 low | Case4 EPA5 2x1 low | Case5 ETU1 1x1
RAN4#80 Assumption [R4-166656] | [16] | [192, 128, 256] | [32] | [192, 128, 256]
Intel[R4-167244] | 32 | 256 | TBD | 192
CATT[R4-167507] | 32 | 256 | 64 | 256
Huawei[R4-167569] | 16 | 256 | 32 | 256
Qualcomm[R4-168041] | 32 | 256 | 32 | 256
ZTE[R4-168158] | 16 | 128 | 32 | 128
Ericsson[R4-168209] | 32 | 256 | 32 | 192
Nokia[R4-168367] | 16/32 | 256/384 | 32 | 192/256
Samsung[R4-168148] | 32 | 256 | 32 | 256

## Slide 4: Agreements
Repetition numbers for NPDCCH demodulation requirements
Repetition numbers for NPDSCH demodulation requirements
Test case | Case 1 EPA5 2x1 | Case 2 ETU1 2x1 | Case 3 EPA5 1x1 | Case 4 ETU1 1x1
Repetition | 64 | 512 | 128 | 1024
Test case | Case 2 EPA5 2x1 | Case 3 ETU1 2x1 | Case 4 EPA5 1x1 | Case 5 ETU1 1x1
Repetition | 32 | 256 | 32 | 256

## Slide 5
Interesting companies are encouraged to provide the results with impairments for NPDCCH and NPDSCH demodulation requirements by RAN4#81.
  Results with impairments should also include the additional impairment due to the omitted DC subcarrier puncturing in the NB-IoT OFDM signal generation.
    Option1 : Companies results with impairment should contain the additional impairments depending on their implementation.
    Option2: Add the common additional impairment value after averaging the results with impairment, such as
      0.3 + X [dB] for NPBCH/PDCCH
      0.5 + Y [dB] for NPDSCH
    Option3: …