## Slide 1: Way forward on UE and BS estimated NF for mm-waves and ITU-R related work
Agenda Item: 10.5.1
Document for: Approval
Source: Ericsson, Sony, Skyworks, Qorvo, Nokia
3GPP TSG-RAN WG4 #80bis Tdoc R4-168770
Ljubljana, Slovenia, 10th – 14th October 2016

## Slide 2: Background
The Noise figure for mm-wave frequencies has been extensively discussed in R4-166526, R4-168530 and R4-168076.
  The Noise Figure is not given by the LNA alone, but also by, bandwidth and dynamic range dependencies as there is a delicate balance .
Beside LNA, typical noise figure contains additional losses due to switches, filters, routing losses, packaging loss, etc (along with some additional margins)
For specification related work in future, full receiver chain, complex relation between noise figure, dynamic range, bandwidths and heat dissipation should be considered.

## Slide 3: Way forward
Proposal 1: The principles outlined below are essential when deriving the Noise Figure (NF) values for mm-waves and should be considered for the mm-waves and ITU-R related work in RAN4.
  The Noise Figure is not given by the LNA alone, but also by, bandwidth and dynamic range dependencies as there is a delicate balance .
  The requirement levels should be carefully adapted to the reasonable levels that the technology can provide in order to facilitate array antennas with many elements.
  Due to compact and highly integrated building practice needed for mm-wave systems with many transceivers and antennas, careful and often complex consideration regarding the power efficiency and heat dissipation in small area/volume is necessary.
  A full receiver chain all the way up to radiating elements should be addressed as all parts in the chain would contribute to the overall receiver performance.

## Slide 4: Way forward (contd.)
Proposal 2: It is assumed that the performance differ less between UE and BS for mm-waves on transceiver level compared to lower frequencies below 6 GHz.
    The estimated NF for both BS and UE are defined as same value for the ITU-R related coexistence simulations.
    It is expected that the BS will have a large number of transceiver necessitating more complex signal routing and hence associated losses. In addition, the filter requirements for BS may be more stringent than the UE, leading to higher losses in the BS receiver chain.
    The larger number of receiver chains and antennas will however result in significantly better OTA BS sensitivity due to combining gains.
  It should be further studied whether different topologies between UE and BS could result in larger difference in performance.
  It should also be studied whether for some UE implementation, the mm-wave antennas could be spread over the physical available area resulting in possibly higher routing losses.

## Slide 5: Way forward (contd.)
  Considering the urgent need for estimated NF for the ITU-R related simulations, RAN4 should assume the provided estimated NF which are best estimates of what the technology will provide.
    Values are preliminary estimations of typical values, not the worst-case and not binding the actual specification values
  Any possible difference between UE and BS NF performance should be carefully considered during the requirement development phase.

## Slide 6: Way forward (contd.)
It is proposed to adopt the following estimated NF values for UE in ITU-R WP5D related coexistence simulations work in RAN4:
  Proposal 3: The estimated UE noise figure for ITU-R related co-existence simulations at 30 GHz should be set to 9 dB.
  Proposal 4: The estimated UE noise figure for ITU-R related co-existence simulations at 45 GHz should be set to 11 dB.
  Proposal 5: The estimated UE noise figure for ITU-R related co-existence simulations at 70 GHz should be set to 13 dB.
For BS:
  Proposal 6: The estimated BS noise figure for ITU-R related co-existence simulations at 30 GHz should be set to 9 dB.
  Proposal 7: The estimated BS noise figure for ITU-R related co-existence simulations at 45 GHz should be set to 11 dB.
  Proposal 8: The estimated BS noise figure for ITU-R related co-existence simulations at 70 GHz should be set to 13 dB.
The above noise figure numbers are intended for ITU-R related coexistence simulations, and can be revised further if needed.