## Slide 1: WF on NB-IoT Measurement Accuracy
Nokia, [Huawei], [HiSilicon], [DoCoMo], [Ericsson], [Intel], [ZTE], [CMCC], [Qualcomm]
R4-168799
3GPP TSG-RAN WG4 #80bis
Ljubljana, Slovenia, 10 – 14 October, 2016
Agenda Item: 6.3.3.1

## Slide 2: Measurement accuracy results (RAN4#80bis)
The results in table are based on companies proposed accuracy values.
Results notes:
  Including margins: Intel, Ericsson, Qualcomm
  Not including margins: ZTE, Nokia, Huawei, CMCC
  Intel measurement period for enhanced coverage: 400ms
  Qualcomm measurement period for normal coverage: 800ms

## Slide 3: Agreement on Measurement period
Following Measurement Periods are preferred by companies:
Agreement on Measurement Periods:
  Normal coverage: 800ms
  Enhanced coverage: 1600ms
Company | Normal mode | Enhanced mode
Intel | 800 | 1600
ZTE | 400 | 800
Ericsson | 800 | 1600
Nokia | 800 | 1600
Huawei | 400 | 800
CMCC | 400 | 800
Qualcomm | 800 | 1600

## Slide 4: Agreement on measurement accuracy
Based on the results provided by companies in RAN4#80bis following is agreed for inband scenario:
  Normal coverage:
    NRSRP: +-[6]dB
    NRSRQ: +-[6]dB
  Enhanced coverage:
    NRSRP: +-[10]dB
    NRSRQ: +-[10]dB

## Slide 5: Way forward
Agreed accuracy numbers are based on in-band scenario
Companies are encouraged for next meeting:
  To verify the agreed numbers
  To verify if agreed numbers can also be applied to non-inband scenarios
In RAN4#81 RAN4 should decide:
  Final agreement on measurement accuracy for in-band scenario
  RAN4 should decide whether measurement accuracy for in-band scenario can also be applied to stand-alone/guard-band scenario
Companies are to provide accuracy numbers for relative NRSRP.