## Slide 1: WF on note 6 in UL CA
Huawei, Hisilicon, LG Electronics, Nokia
R4-168853
3GPP TSG-RAN WG4 Meeting #80BIS
Ljubljana, Slovenia, 10th – 14th October, 2016

## Slide 2: Background
WF on 3DL/2UL support was agreed in RAN4#75: R4-153931
All Low+High 2UL CA combinations shall be supported
  i.e. LH and L’H in UL for LL’H terminal and LH and LH’ in UL for LHH’ terminal
Low+Low and High+High combinations support is optional
If UE supports Low+Low or High+High combinations in UL, then UE shall support Low+High combinations
The above applies for 2UL combinations without IMD issues or close proximity tx-rx
For close proximity tx-rx combinations, this is related to Pcell discussion. So support is FFS
For 2UL combinations with harmonic issues, this is related to Pcell discussion. So support is FFS
For 2UL combinations with IMD issues, support is optional
It is also expected that as the state-of-the-art technology evolves in the future, mandatory support of 2UL combinations with IMD issues can be possible.
Agreement is to capture this in the specification. TBC how to do it. Aim August meeting to introduce in the spec
This agreement was done only for 3DL/2UL, not for 2DL/2UL
At the time of making this agreement, 4DL/2UL and/or 5DL/2UL did not exist
L stands for frequencies up to 960MHz
H stands for frequencies from 1710MHz

## Slide 3: Current situation
Note 6 exists in 2DL/2UL, 3DL/2UL, 4DL/2UL CA configuration Table 5.6A.1-2, Table 5.6A.1-2a and Table 5.6A.1-2b respectively
There are UL CA configurations marked with note 6 even there is IMD issue
  UL_CA_1A-8A
  UL_CA_3A-8A
  UL_CA_5A-7A
  UL_CA_7A-20A
Some combinations have errors with respect to note 6 applicability
  UL_CA_1A-28A has note6
  UL_CA_1A-18A does not have note6
Treatment of mid bands (11,21) varies
  UL_CA_21A-42A has note 6

## Slide 4: WF proposal
Note 6 is not applied for 2DL/2UL (Table 5.6A.1-2) and shall be removed
Note 6 shall apply also for 4DL/2UL (Table 5.6A.1-2b) and 5DL/2UL (once specified)
Treatment of harmonic cases shall be discussed in next meeting
Note 6 shall be removed from the combinations that are not aligned with agreed WF R4-153931.
Note 6 wording improved:
  Current: If the UE supports uplink CA for corresponding downlink CA it shall support this uplink CA configuration
  New: If the UE supports any uplink CA configuration for corresponding downlink CA configuration it shall support this uplink CA configuration
These changes shall be captured in upcoming CR’s

## Slide 5: Reference
[1] R4-153931, “Way forward for 3DL/2UL support”, Vodafone