## Slide 1: WF on MPR/A-MPR requirement and in-band emission for UL 256QAM
Huawei, Hisilicon, Skyworks, Qualcomm, Nokia, Ericsson
3GPP TSG-RAN WG4 Meeting #80bis R4-168870
2016Ljubljana, Slovenia, 10 – 14 October, 2016

## Slide 2: Background
MPR results are provided by the following contributions
  R4-167675, MPR requirement on single carrier for UL 256 QAM, Huawei, Hisilicon.
  R4-167677, MPR impaction by in-band emission for UL 256 QAM, Huawei, Hisilicon.
  R4-167906, Simulation results for UL 256QAM MPR, Ericsson
  R4-168074, Required MPR for UL 256QAM support, Skyworks Solutions Inc
  R4-168093, UL256QAM MPR, Qualcomm Incorporated
  R4-168869, Uplink 256-QAM MPR simulations, Nokia

## Slide 3: Background -> MPR
MPR for contiguous allocation for UL 256QAM proposed by companies
 | Channel bandwidth / Transmission bandwidth (NRB) |  |  |  |  |  | MPR (dB)
 | 1.4 MHz | 3.0 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 
Ericsson | ≥ 1 |  |  |  |  |  | ≤ 3
Skyworks | ≥ 1 |  |  |  |  |  | ≤ 3.7
Nokia | ≤ 5 | ≤ 4 | ≤ 8 | ≤ 12 | ≤ 16 | ≤ 18 | ≤ 4
 | > 5 | > 4 | > 8 | > 12 | > 16 | > 18 | ≤ 5
Huawei | ≤ 5 | ≤ 4 | ≤ 8 | ≤ 12 | ≤ 16 | ≤ 18 | ≤ 5
 | > 5 | > 4 | > 8 | > 12 | > 16 | > 18 | ≤ 6
Qualcomm | ≤ 6 |  |  |  |  |  | ≤ 6
 | >6 and ≤ 50 |  |  |  |  |  | ≤ 7
 | > 50 |  |  |  |  |  | ≤ 8
Companies have noticed that RB threshold per BW may not be relevant to MPR anymore

## Slide 4: Background -> MPR
MPR for un-contiguous allocation for UL 256QAM proposed by companies
 | MA | Allocation ratio
Qualcomm | 8 | 0 < A < 0.6
 | 10 | 0.6 ≤ A < 1
Ericsson | 8.00-10.12A | 0 < A < 0.33
 | 4.66 | 0.33 ≤ A < 1.00
Nokia, Huawei | 8.00-10.12A | 0 < A < 0.3
 | 5 | 0.3 ≤ A < 1.00

## Slide 5: Background -> In-band emission
Views on the in-band emission for UL 256QAM from companies
  Nokia: The currently specified carrier suppression of 25 dB is insufficient for 256-QAM. A suitable value should be found and specified.
  Qualcomm: Extend the existing definition for non-contiguous allocations
  Huawei: In-band emission shall have no impaction to MPR

## Slide 6: WF on MPR/A-MPR requirement
MPR for single carrier:
  For contiguous allocation
  MPR for non-contiguous allocation is FFS
    More measurement results and studies are encouraged to be provided by companies
A-MPR for single carrier
  Keep A-MPR requirement unchanged
Modulation | Channel bandwidth / Transmission bandwidth (NRB) |  |  |  |  |  | MPR (dB)
 | 1.4 MHz | 3.0 MHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 
64 QAM | ≤ 5 | ≤ 4 | ≤ 8 | ≤ 12 | ≤ 16 | ≤ 18 | ≤ 2
64 QAM | > 5 | > 4 | > 8 | > 12 | > 16 | > 18 | ≤ 3
256 QAM | ≥ 1 |  |  |  |  |  | ≤ 5

## Slide 7: WF on MPR assumptions->In-band emission
For UL 256QAM
  In-band emission shall be further studied and have no impaction to MPR
  In-band emission modifications will be considered after MPR agreement.