## Slide 1: WF on Co-existence Study between NB-IoT and CDMA
Samsung, China Telecom, Qualcomm, Ericsson , Huawei
3GPP TSG-RAN WG4 Meeting #80Bis
Ljubljana, Slovenia, 10 - 14 Oct, 2016
Agenda Item: 9.3
Document for: Approval
R4-168920

## Slide 2: Background
In RAN4 #80, the details of coexistence simulation methodology and parameters are agreed in WF R4-166994.
In this meeting, companies have provided simulation results and their analysis on whether or not Rel-13 NB-IoT RF requirements is able to ensure the co-existence between NB-IoT and CDMA.
Agreement from RAN4#80Bis main session:
  Rel-13 NB-IoT BS ACLR requirement is stringent enough to guarantee the protection for CDMA system, and no additional requirement is required.
  Rel-13 NB-IoT BS ACS requirement is stringent enough to guarantee the coexistence with neighboring CDMA system, and no additional requirement is required.

## Slide 3: Way Forward
Conclusion can be made based on submitted simulation results in RAN4#80Bis:
  Rel-13 NB-IoT BS ACLR requirement can guarantee the protection for CDMA system, and no additional requirement is required.
  Rel-13 NB-IoT UE ACS requirement can guarantee the coexistence with neighboring CDMA system, and no additional requirement is required.
  Rel-13 NB-IoT BS ACS requirement can guarantee the coexistence with neighboring CDMA system, and no additional requirement is required.

## Slide 4: Way Forward
RAN4 will study whether the achievable ACLR value obtained from Rel-13 NB-IoT UE RF requirement can guarantee the coexistence with CDMA, with following method to obtain the achievable ACLR values from Rel-13 requirement:
  Using NB-IoT UE spectrum emission mask specified in Table 6.6.2F.1-1, with 385kHz edge to edge separation for CDMA, i.e., around 49dB ACLR (integrated over 180kHz adjacent channel frequency based on the emission mask with 23dBm assumed for Tx power).
The way to determine the required ACLR value for coexistence with CDMA from submitted simulation results:
  FFS.

## Slide 5: Way Forward
Companies are encouraged to check the simulation and bring results in RAN4 #81 for further alignment and analysis, by focusing on the following scenario:
  Scenario-2: DL NB-IoT BS interfere to CDMA UE.
  Scenario-3: UL NB-IoT UE interfere to CDMA BS.
For better alignment and more time for company to perform analysis, companies should provide their updated simulation results for Scenario 2 and 3, over RAN4 email reflector before 31th Oct. (one week before RAN4#81 contribution submission deadline).
In RAN4 #81, RAN4 should make the conclusion on whether or not Rel-13 NB-IoT UE RF requirement can satisfy the coexistence with legacy CDMA system.