## Slide 1: WF on MIB acquisition delay
Qualcomm
3GPP TSG-RAN WG4 Meeting #80bis, Ljubljana, Slovenija, 10th – 14th October 2016
R4-168971

## Slide 2: Agreements from RAN4 80bis eMTC Ad-hoc
MIB delay in following requirements is included as variable (T_MIB):
  Paging interruption
  HO delay
  RRC re-establishment
  Other requirement if it is identified that MIB is needed
Intention is to agree on core requirements involving MIB will be agreed in this meeting
Results are needed for test cases assuming 99% probability for test cases.

## Slide 3: MIB acquisition and candidate receiver algorithm
MIB TTI = 40ms
Candidate algorithms to acquire MIB
  Baseline: The “keep trying” decoder is definition is: The decoder simply “keeps trying” to decode the transmitted Rel-13 eMTC PBCH frames until the decoder eventually gets lucky and decodes it correctly. With this solution there is a trade-off between coverage gain and decoding time (i.e. the number of decoding attempts). [Refer to R1-132908]
  Other algorithms are not precluded
MIB acquisition delay = 99%-ile of the number of frames required to successfully decode the MIB in the worst case channel (among the channels in considered in WF for each CE mode/coverage level)
To obtain MIB acquisition delay, companies are encouraged to provide CDF of MIB acquisition time based on the simulation assumptions in slide 4 & 5

## Slide 4: Simulation assumptions for Mode A/normal coverage
Parameter | Case 1 | Case 2 | Case 3 | Case 4
Sys BW | 10MHz | 10MHz | 10MHz | 10MHz
Duplex Mode | FDD | FDD | TDD | TDD
Channel | EPA5 | ETU30 | EPA5 | ETU30
SNR | -6dB |  |  | 
Repetition of PBCH | Enabled |  |  | 
Antenna Configuration & Correlatiom | 2x1 low |  |  | 
UE frequency error | 100Hz |  |  | 
Companies are also encouraged to provide results with implementation margin to reflect worst case acquisition delay

## Slide 5: Simulation assumptions for Mode B/enhanced coverage
Parameter | Case 1 | Case 2 | Case 3 | Case 4
Sys BW | 10MHz | 10MHz | 10MHz | 10MHz
Duplex Mode | FDD | FDD | TDD | TDD
Channel | EPA1 | ETU1 | EPA1 | ETU1
SNR | -15dB |  |  | 
Repetition of PBCH | Enabled |  |  | 
Antenna Configuration & Correlatiom | 2x1 low |  |  | 
UE frequency error | 100Hz |  |  | 
Companies are also encouraged to provide results with implementation margin to reflect worst case acquisition delay