## Slide 1
The following slide set contains items discussed at the Thursday (13 Oct) and Friday (14th Oct) adhocs on multi-node testing, and the minutes (see the comments field below the slides)
3GPP TSG-RAN WG4 Meeting #80Bis R4-168999
Ljubljana, Slovenia, 10-14 October, 2016
Title: Minutes of RAN4#80bis adhoc meetings on multi-node testing
Agenda item: 7.1.1
Document for: Approval

## Slide 2: Way Forward on additional issues related to multi-node tests for LAA
Ericsson, Qualcomm Incorporated, Huawei, Nokia, …
3GPP TSG-RAN WG4 Meeting #80Bis R4-168893
Ljubljana, Slovenia, 10-14 October, 2016

## Slide 3: Background
In RAN4#80 and RAN4#79, two way forwards [1], [2] on multi-node tests have been agreed.
Two tests has been agreed, namely:
  Throughput test (related to channel access priority class 3)
  Outage test (related to channel access priority class 1)
[1] R4-166971, WF on LAA Multi-node test
[2] R4-164971 WF on LAA co-existence testing

## Slide 4: Choice of devices
For IEEE 802.11 devices to be used in the test, both APs and STAs, they should be representative and taken off the shelf
  For IEEE 802.11 APs and STAs, the devices should come from multi-vendor and multi-standard (i.e. multi-generation IEEE 802.11 systems).
For LAA:
  LAA BS supplied by vendors
  LAA UEs should be representative and taken off the shelf
Original version

## Slide 5: Choice of devices
All 802.11 devices should be commercially available and not reference design
For IEEE 802.11 devices to be used in the test, both APs and STAs, they should be representative and taken off the shelf
  IEEE 802.11 APs and STAs, should be selected representing the devices should come from multiple vendors and multiple generations of the 802.11 standard. -standard (i.e. multi-generation IEEE 802.11 systems).
  Devices shall be selected from 802.11n and 802.11ac.
For LAA:
  LAA BS supplied by vendors
  LAA UEs should be representative “commercially available” or “ready for market” and taken off the shelf
Agreed
Notes: HPE: three very important issues, all parties 802.11 devices commercially devices, included device multiple vendors, fine to accept 11n as well as 11ac. Main point of contention is “off the shelf”: means no changes in the devices be made, hard time to accept. Agreements on the words desired.
CableLabs: another reason for changing off the shelf, the DUT should be commercial and not reference designs. Off the shelf is ambiguous
Ericsson: the criterion commercially available and off the shelf is the same thing, can we add something like “commercially available and not reference designs?
HPE: what is clear with “off the shelf”, we would be happy with “commercially available and not reference designs, acceptable to Ericsson and Qualcomm? Can we discuss what off the shelf hardware means?
Qualcomm: choice of devices refers to hardware, but the main concerns is off the shelf software configuration,
Verizon: we would like to see “real life device”, we don’t want anything particular for testing
HPE: like to defer to later discussion on device parameter setting, should not be reference designs, devices you can purchase and deploy. Open to proposal from QC and Ericssson.
Chair: “commercially available and not reference design (see slide on device parameter settings)
Verizon: commercially available means many types of devices, need clarification
BCM: see parameters for device parameter settings, why tie this together?
Ericsson: keep the sentence on 11n and 11ac for the time being
BRM: stays as FFS?
Ericsson: come back to this tomorrow, we keep the brackets.
BCM: BCM has a concerns on multiple generations only if 11n or 11ac. Then also multiple generations in brackets.
HPE: why not change for LAA
Ericsson: this has no meaning for LAA since conformance tested
Ericsson: we are fine to remove the square brackets on the selection of 802.11 devices

## Slide 6: Test Setup
Note: as updated in TP: R4-16xxxx
The following test setup is assumed to be a baseline for further discussions:
Circulator needed here
Small details remain
Notes: CableLabs: in agreement, small details remain.

## Slide 7: Test cases
Note: as detailed in revised TP
Other traffic cases are FFS
The purpose of the test when WiFi is the aggressor is to help 3GPP to validate LAA and enhancement of system performance; there will be no pass/fail criterial for WiFi (AGREED)
Scenario | Victim system |  | Aggressor system |  |  |  | Traffic Type for both victim and aggressor
 | Victim device to be tested | Companion victim device | Aggressor device in baseline | Companion aggressor device | Aggressor device to be tested | Companion aggressor device | 
1 | Wi-Fi AP | Wi-Fi STA | Wi-Fi AP | Wi-Fi STA | LAA BS | LAA UE | Best effort
2 | Wi-Fi AP | Wi-Fi STA | Wi-Fi AP | Wi-Fi STA | LAA BS | LAA UE | Voice
3 | LAA BS | LAA UE | LAA BS | LAA UE | Wi-Fi AP | Wi-Fi STA | Best effort
4 | LAA BS | LAA UE | LAA BS | LAA UE | Wi-Fi AP | Wi-Fi STA | Voice
To be discussed
Notes: HPE: two major considerations, shows Wi-Fi best effort tested in the presence of best effort and voice, our suggestion is other configurations where Wi-Fi voice is tested in the presence of LAA best effort. No criterion for pass criterion for Wi-Fi, we would like to see some furhter discussions to clarify.
BCM: more effective to treat the traffic type together
Qualcomm: we should include this table since mandate from RAN
HPE: very happy to include the table with the note
Verizon: we agree with Qualcomm comment.
Chair: Verizzon and HPE work on the sentence (the FFS)
BCM: slide 6 and 7 merged [discussion on mixed traffic cases not captured]
Huawei: are sufficient now for covering the SI
Chair: put other traffic cases FFS.
BCM: put full buffer

## Slide 8: Traffic cases
WiFi to WiFi best effort
  Best effort WiFi  best effort WiFi
  Best effort WiFi  VoIP WiFi
LAA to WiFi best effort
  Best effort LAA  best effort WiFi
  Best effort LAA  VoIP WiFi
WiFi to WiFi VoIP
  VoIP WiFi  VoIP WiFi
  VoIP WiFi  best effort WiFi
LAA to WiFi best effort (for LAA devices that support VoIP)
  VoIP LAA  VoIP WiFi
  VoIP LAA  best effort WiFi
WiFi will use bi-directional voice traffic
Best effort traffic will be full buffer UDP
NOTE: Other traffic cases are FFS
To be discussed
(6 and 7 together)
Notes: Qualcomm: the purpose of the test from Wi-Fi to LAA is to understand the impact of WiFi to LAA , that’s it
HPE: does that mean pass/fail meets some performance in the presence of wi-Fi?
Qualcomm: the pass/fail is exactly the same, it has no implication of wifi equipment, what is the impact of a particular device. Test is completely symmetric, nothing hidden.
Nokia: study item to study the direction of the coexistence, also wifi to LAA.
CableLabs: WFA define compliance for Wi-Fi devices. Not clear if RAN4 should do this?
BCM: is it OK to define evaluation test for WiFi, BCM agrees for evaluation purposes, not pass/fail for Wi-Fi
Verizon: objective is coexistence, very clear. Can help us understand the weakest point. Clear to comparison
Ericsson: in RAN4 we have many test to test external interferers, not for determining pass/fail
Nokia: this is clearly stated in second bullet of the SI, reason for cross technology
HPE: we have a lot of detail about the proposals how wifi-wifi etc DUT testing be performance and how to run those tests, the particlar combination of WiFi aggressor need more study.
Qualcomm: we are goinground, clear we need to du symmetric test, we agree WFA is testing WiFi devices, but as victims. Not only WiFi as victims. Unfair only one system as victim, maybe we can call it evaluation instead of pass/fail
BCM: []
Qualcomm: redefining the 11n and 11ac is completely out of scope, the scope should be clear
CableLabs: evaluation testing is usually done in private mode, this could be done in private sessions. WiFi against LAA should be compliance?
Huawei: it’s clear in the objective in the SI should be bi-directional, fair to test wifi as aggressor
HPE: we are not suggesting that the performance of LAA in the presence of WiFi should not be tested, but how to be done and what to do with the results. No further descriptions today, keep it for item for further study
Verizon: remove the VoIP LAA aggressor case
Huawei:

## Slide 9: Device parameter settings
The tests shall ensure repeatability and representative operational behavior.
The starting point of the configuration of both 802.11 and LAA equipment shall be based on the default settings
Any modifications compared to the default settings if needed are FFS and shall be documented.
Remove
Notes: Qualcomm: the baseline setting should be thedefault settings, there could be some modification needed for 1) run the test 2) reprodicibility 3) oeprational behaviour. We are willing to compromise a bit, whatever we include needs to be clear and effective. No ambiguity.
HPE: we are happy with language in slide 9 and prepared to go with that

## Slide 10: Device parameter settings
The tests shall ensure repeatability and representative operational behavior.
The starting point of the configuration of both 802.11 and LAA equipment shall be based on the default settings.
If needed, modifications to the default settings to achieve the test objectives of repeatability and representative operational behavior, shall be documented [HPE can work with QC on the text]
The above modifications, if needed, are FFS
Remove
Notes: Qualcomm: problem is if ”documented” is needed? We can discuss further
BCM: this slide has been agreed offline

## Slide 11: Device parameter settings
The tests shall ensure repeatability and representative operational behavior.
The starting point of the configuration of both 802.11 and LAA equipment shall be based on the default settings.
In order to achieve the test objectives of repeatability and representative operational behavior, modifications to the default settings might or might not be needed
The above modifications, if needed, are FFS
Modifications compared to the defaults settings, if any, shall be documented
Agreed

## Slide 12: Throughput Tests: Rx levels (current proposals)
Proposed RX levels in dBm
  -72+∆1 and -82-∆2 (R4-168545)
  -62+∆ and -82-∆ (R4-167653)
  -62 ±∆ and -82 ±∆ (R4-165830)
  -62 and -82 (R4-168405)
  -57dBm, -67dBm, -77dBm, -82dBm(R4-167941)
No agreement
Include in TP
Notes: CableLabs: take of the -62 and -82
Nokia: not take it out
Ericsson: maximum two levels.
HPE: no particular view of levels, one level that is in between -72 and -82, difficult to get reliavle test results at levels that are as low as -82
BCM: agree with HPE
Nokia: LBT test is with -72 in the conformance test
Qualcomm: no substantial difference between -77 dBm and -82 dBm,
HPE: unlikely that there is substantial difference between -82 and -77 therefore we would to agree with Qualcomm that the level below should be no substantial difference between -77 dBm and -82 dBm,
CableLabs: agree with the justification of Qualcomm and HPE
Ericsson: one level with -72 and another should be -82
HPE: considering that QC and CableLabs that there is no substantial difference between -77 and -82, there may be unusual cases we would strongly recommend we choose -77
Huawei: WiFi and LAA has the same behaviour
Nokia: we considered all proposals, in each proposal -82
BCM: we would like to say, -57, -67 etc, the proposal is to include all the cases
Ericsson: important to limit the test cases
BCM: we should select realistic test cases
Chair: -57dBm, -67dBm, -77dBm?
QC: surprise there is no -82 dBm
BCM: supports chair
HPE: supports chair
CableLabs: we support the proposal
Nokia: Not agree three levels
Ericsson: agree with Nokia
BCM: support the chair proposal
Ericsson: -77 dBm LAA may not be fair to WiFi
Qualcomm: more discussions

## Slide 13: Throughput Tests: target operating point (current proposals)
SNR/SINR/SIR levels
  SINR=15dB (R4-168545)
  SNR=16dB (R4-167653)
  SIR=15dB (R4-165830)
  SIR=0dB (R4-167941)
  SINR = 0dB(R4-168405)
Include in TP
Notes: HPE: likelihood to reach agreement is low here
BCM: ok to have test at multiple levels, prefer 0 dB
HPE: whatever test level we set is irrelevant, set the wanted traffic and interferer relatively close to each other
Qualcomm: will include both the SIR and levels in the TP.

## Slide 14: Throughput Tests: pass fail criteria (current proposals)
Pass fail criteria
  Median of recorded throughput CDF (R4-168545)
  Mean of the recorded throughput CDF (R4-165830)
  Normalized best effort throughput and at {5%ile, 25%ile, 50%ile, 75%ile, 95%ile} (R4-167941)
  Mean of the recorded throughput CDF (R4-168405)
Accuracy for pass/fail criteria
  10%
More than pass/fail criteria can be considered
Under consideration

## Slide 15: Outage test
Similar to throughput test
  Test setup
  Choice of devices
  RX levels
  Operating point
Traffic cases
  VoIP traffic in both links
Pass/fail criteria:
  What is the metric?
    What percentage of packets lost within a period of time? How many times of burst packet loss? i.e. 3 consecutive packets lost within certain time?
    Jitter
    Latency
Under consideration