## Slide 1: WF on TM10 UE CRS-IM gain Testcases
Intel, Huawei/HiSilicon, Qualcomm, Samsung, LG
R4-158195
3GPP TSG-RAN WG4 Meeting #77
Anaheim, USA, 16 – 20, Nov. 2015

## Slide 2: TM10 Performance requirements
Performance requirements are based on 2-cell CRS-IC for TM10 gain test.

## Slide 3: Results for alignment
Interested companies are encouraged to provide simulation results and impairment results for all gain tests before Dec.19 2015. It includes:
  TM10 (one-CSI-process) (both for FDD and TDD)
  TM10 (multiple-CSI-process) (both for FDD and TDD)

## Slide 4: For TM10 one-CSI-process UE test
8.45 dB is taken as the interference level for the aggressor cell outside the CoMP set
MCS=16 is used for the MCS setup for the TM10 one CSI process test.

## Slide 5: For TM10 Multiple-CSI-Process test
Employ PDSCH scheduling with DPS in TM10 CRS-IM test for multiple CSI process UE
Use INR1=10.45dB and INR2=8.45dB to mandate CRS-IM operation for neighbor cells both inside CoMP set and outside CoMP set.
Use the same transmission power for TP2 and TP1

## Slide 6: For TM10 multiple-CSI-process test
MCS=16 is used for the multiple-CSI-process test

## Slide 7: TM10 UE CRS-IC capability Report
TM10 capability report and non-TM10 capability report introductions are separate.
RAN4 sends LS to RAN2 to introduce an Rel-13 UE capability report signaling to support the TM10 UE CRS-IC RX.
  TM10 UE capability signaling indicates CRS-IM support on at least one CC.