## Slide 1: Way forward on antenna isolation
TeliaSonera
3GPP TSG RAN WG4 #77 R4-158445 Anaheim, USA, 15th-22th November 2015

## Slide 2: Background
RAN4 will work on resolving the issue of discrepancy between conductive requirements and tests due to large antenna port isolation in conductive tests
Scope of the work is limited for cases where antenna isolation value assumed in simulations have big impact on requirements. These are (at least)
  2 UL interband CA Class A4 MSD
  2UL / 3DL MSD
  2DL/1UL CA

## Slide 3: Proposal on antenna isolation issue
Proposed methods to be discussed further in RAN4#78 where decision is expected to be done for Method (1) or Method (2)
  1) Method
    MSD requirements are calculated only for main receiver
    No signal is feed to diversity receiver in test cases part of this WF
    Interested companies recalculate existing MSD requirements for main receiver only
    This new approach is applied from REL-14 onwards
  2) Method
    Alternatively, keep the test set as it is and MSD requirements are re-calculated with large antenna port isolation
    This new approach is applied from REL-14 onwards
Issues to be discussed in RAN4#78
  How to handle the case that UE has 2 main antenna ports
  Is the diversity receiver port left open or terminated in 50 ohm
  Discuss if existing requirements are maintained in the spec and how