## Slide 1: 3GPP TSG-RAN WG4 Meeting #80bis Ljubljana, Slovenia, 10th – 14th Oct, 2016
Qualcomm, Huawei,HiSilicon
Way forward on NB-IoT transmission signal pattern for NPDSCH demodulation performance
R4-168947

## Slide 2: Background
During RAN4#80, WF R4-167075 about NPDSCH transmission pattern was agreed with the following options:
  Option 1: Use different Noc levels for NPDCCH and NPDSCH
    For the details see the next pages
  Option 2: Use larger repetitions for NPDCCH and keep Noc level constant in the whole test
  Option 3: Other options are not precluded

## Slide 3: Agreed Transmission signal pattern
To ensure the NPDCCH performance during the NPDSCH test
Use larger repetitions for NPDCCH and set Noc level as follows:
  Set -93dBm/15kHz for Noc in NPDSCH subframe
  Set -99dBm/15kHz for Noc level in NPDCCH subframe
    Noc should be -99dBm/15kHz for overhead channels as well during NPDCCH transmission
Ensure NPDCCH BLER <= [3]%
The impact of NPDCCH BLER on NPDSCH performance should be considered when providing impairment simulation results.
  Option 1: Multiply NPDSCH throughput results with [97]% to account for [3%] NPDCCH BLER
  Other options are not precluded.

## Slide 4: NPDCCH Repetitions for each NPDSCH Demod Test
Simulation number | Band-width and MCS | Deployment Mode | (ITBS, ISF) (Table 6) | NPDSCH Repetition level | Propagation Condition | NPDCCH Repititions | Number of NRS ports | Target SNR (dB)
1 | 180KHz QPSK [1/3] | In-band | ([4], [0]) (TBS=56bits) | 1 | [EPA5] | [8] | 2 | TBD
2 | 180KHz QPSK [1/3] | In-band | ([4], [0]) (TBS=56bits) | 32 | [EPA5] | [16] | 2 | [-6]
3 | 180KHz QPSK [1/3] | In-band | ([4], [0]) (TBS=56bits) | 256 | [ETU1] | [128] | 2 | [-12]
4 | 180KHz QPSK [1/2] | Standalone/Guard-band | ([9], [3]) (TBS=616bits) | 32 | [EPA5] | [32] | 1 | [-6]
5 | 180KHz QPSK [1/3] | Standalone/Guard-band | ([6], [3]) (TBS=392 bits) | 256 | [ETU1] | [256] | 1 | [-12]