## Slide 1
R4-160675
WF for NB-IOT transmitter characteristics

## Slide 2: Background
This contribution captures the intial agreements for NB-IOT transmitter characteristics which were endorsed in RAN4 NB-IOT Ad-Hoc in Budapest. Background information for agreements can be found from listed references.
This contribution also lists topics that needs further discussion in next meeting.
REFERENCES:
R4-77AH-IoT-0059, NB-IOT UE RF aspects, Nokia Networks

## Slide 3: NB-IOT Transmitter characteristics agreements
At least Maximum output power classes 3 (23 dBm) is specified for NB-IOT.
  Power class 5 can be discussed in the next meeting.
Minimum output power is specified to be -40 dBm over NB-IOT channel bandwidth
  for UE that supports multitone, this is defniend for fully allocated channel.
  For UE that supports single tone, it is FFS.
Transmit Off power is specified to be -50 dBm over NB-IOT channel bandwidth
  for UE that supports multitone, this is defniend for fully allocated channel.
  For UE that supports single tone, it is FFS.
Frequency error is specified to be [±0.1] PPM observed over a period of one time slot compared to the carrier frequency received from the NB-IOT BS
NB-IOT UE to UE co-ex clause refers back to E-UTRA requirement
Occupied bandwidth shall be less than NB-IOT channel bandwidth i.e. 200 kHz
  Follows the decision on NB-IOT channel bndwidth discussion

## Slide 4: NB-IOT Transmitter characteristics agreements
E-UTRA General ON/OFF time mask can be re-used for NB-IOT
E-UTRA Absolute power tolerance requirement can be re-used for NB-IOT
E-UTRA Relative power tolerance requirement can be re-used for NB-IOT
E-UTRA Aggregate power control tolerance requirement can be re-used for NB-IOT
E-UTRA QPSK EVM requirement 17.5% can be re-used for multitone Unrotated QPSK NB-IOT

## Slide 5: NB-IOT Transmitter characteristics open issues
MPR, A-MPR
  Emission requirements are needed and alined PA simulation assumption is also needed.
EVM
  Measurement method is FFS.
  Study if single tone pi/2 BPSK requirement is needed
  Single tone pi/4 QPSK requirement
  Incase RAN1 agrees more modulation schemes those will be studied as well
SEM
  GMSK mask might not be suitable becasue of different modulaiton.
ACLR
  Comes from co-ex simulations
General Spurious emissions
  What is the boundary between OOB and General spurious emissions, for example 250% of channel bandwidth
  LTE general spurious emission requirements are applied

## Slide 6: NB-IOT Transmitter characteristics open issues
Additional spurious emissions
Carrier leakage requirement
In-band emission requirement
EVM equalizer spectrum flatness requirement
  Discuss the need for narrowband system.
transmit intermodulation requirement
  Discuss the need for narrowband system. GSM does not have one.