## Slide 1: WF on BS MMSE-IRC receiver in asynchronous network
China Telecom, Huawei, ZTE, Nokia Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 Meeting #78 St. Julian’s, Malta, 15 - 19 Feb, 2016
Agenda Item: 6.6.1
R4-161169

## Slide 2: Background
BS MMSE-IRC receiver in asynchronous network has been extensively discussed in previous RAN4 meetings.
In RAN4 #76bis, it was agreed that:
  Consider investigating the performance of asynchronous network as well as synchronous network in BS MMSE-IRC WI [1].
  Decision on the need of specifying requirements for asynchronous network to be made in RAN4 #78 [2].
In RAN4 #77, it was agreed that:
  Interference model [3] [4]:
    Keep Option 1, Option 2 and Option 3 open.
    Have further evaluations and make decision on the interference model in RAN4 #78.
    Note: Details of the three options are provided in the Annex.

## Slide 3: Way Forward
Proposal 1: RAN4 to specify BS MMSE-IRC demodulation requirements for asynchronous network operation, with the following test cases.
Proposal 2: Select option 3 as asynchronous network interference model.
Num | Bandwidth | MCS | Propagation condition (Serving, interferers) | Antenna configuration for serving and interferers | Scenario | (DIP1-1, DIP1-2) dB
 |  |  |  |  |  | Interference model: option 3
2 | Six bandwidths, full PRB allocation | 6 | (EPA5, ETU5) | 1x2 Low | HetNet | (-0.43, -0.43)
4 |  | 15 | (EPA5, ETU5) | 1x4 Low | HetNet | (-0.43, -0.43)
6 |  | 20 | (EPA5, ETU5) | 1x8 Low | HetNet | (-0.43, -0.43)

## Slide 4: References
[1] RAN4 #76bis meeting report.
[2] R4-155442, China Telecom, Work plan on performance requirements of MMSE-IRC receiver for LTE BS (version 3), RAN4 #76bis, Oct 2015.
[3] R4-158116, Ad hoc minutes for MMSE-IRC receiver for LTE BS, Huawei, China Telecom, RAN4 #77, Nov 2015.
[4] R4-158385, WF on interference modelling for BS MMSE-IRC in asynchronous network, ZTE, China Telecom, Samsung, NTT DOCOMO, RAN4 #77, Nov 2015.

## Slide 5: Annex: Options for asynchronous network interference model (1)
Option 1: Modelling of time-varying interference in terms of interference power and fast fading
  Configure two ON/OFF interfering signals (UEs) to model the interference from one dominant interfering cell, i.e., the dominant interfering cell schedule UE 1-1 in the even TTIs and schedule UE 1-2 in the odd TTIs. The interference power of UE 1-1 and UE 1-2 are different, and different channel seeds are used for the desired UE and interfering UEs.
  As baseline, the transmission of the interference signal is delayed with respect to the desired signal by 0.33 ms.
Figure A-1: Modeling of time-varying interference: One explicit interfering cell

## Slide 6: Annex: Options for asynchronous network interference model (2)
Option 2: The only difference compare to the synchronous simulation setup is to model certain timing offsets
  Model two simultaneous interfering UEs, and the transmissions from the first/second dominant interfering UE is delayed with respect to the desired UE by 0.33/0.67 ms.
  Note: model only one interfering UE for 2Rx cases.
Figure A-2: Two simultaneous interfering UEs

## Slide 7: Annex: Options for asynchronous network interference model (3)
Option 3: Modeling of time-varying interference in terms of fast fading
  The only difference compared to Option 1 is that the interference power of UE 1-1 and UE 1-2 are the same.