## Slide 1: WF on DL Control Channel IM Interference models
Huawei, HiSilcon, Intel Corporation
3GPP TSG-RAN WG4 Meeting #78 St. Julian’s, Malta, 15 – 19 February, 2016
Agenda Item: 6.4
R4-161171

## Slide 2: Background
In RAN4 #77 meeting, two WFs were approved for interference modelling
  WF R4-158135 was approved to capture agreements on DL Control Channel IM Interference model;
  WF R4-158136 was approved to capture agreements on DL Control Channel IM Link-level simulation assumptions

## Slide 3: Way Forward (1)
Interference power profile
  Baseline: High INR (I1/Noc = 13.91 dB, I2/Noc = 3.34 dB)
  Other options are not excluded if technical issue is identified
  Aggregation CCE level for serving PDCCH
  [2] for CRS-colliding case
  [4] for CRS-non-colliding case

## Slide 4: Way Forward (2)
Interference model for PDCCH/PCFICH/PHICH IM receiver in synchronous networks
  CFI values for serving cell and interference cell
    eIRC + CRS-IC: CFIS = 1, CFII = 1
    IRC + CRS-IC : CFIS = 1, CFII = 1 ; CFIS = 3, CFII = 1 ; CFIS = 3, CFII = 3
  PDCCH/PHICH interference structure
    random QPSK-modulated symbols with the SFBC-based precoding.
  PDCCH/PHICH interference loading
    50% loading level
  PDCCH/PHICH power boosting
    Non-uniform power boosting with random value from -6dB to 6 dB
  Interference presence and power boosting modeling granularity is FFS
    Option1 per-REG
    Option2 per-CCE
    Down-selection is done in next meeting, companies are encouraged to provide more inputs

## Slide 5: Way Forward (2)
Interference model for PDCCH/PCFICH/PHICH IM receiver in synchronous networks
  PDSCH interference model
    CFIS ≤ CFII: PDSCH is emulated via OCNG with 100% loading
    CFIS > CFII: Per-PRB partial level model with 50% loading is used. Reuse Rel-11 Type A receiver (TM4) interference model parameters (RI, modulation, precoding)

## Slide 6: Way Forward (3)
Interference model for ePDCCH IM receiver in synchronous networks
  Interference model 1
    No PDSCH present
  Interference model 2
    Reuse PDSCH interference parameters from Rel-11 Type A receiver requirements (test case 8.3.1.1A). The probability of occurrence of transmission rank 1, 2 is 80% and 20%, respectively.

## Slide 7: For Information
Per-CCE level PDCCH Interference presence and power boosting modeling (refer to model 2 in R4-160756, section 3)
  Achieve the available CCEs for interference cell PDCCH based on CFI and PHICH configuration, marked as CCE_0, CCE_1, …, CCE_N-1
  With given the partial loading ratio X%, get the number of empty CCE: M
  Apply the zero power for CCE_0, CCE_1, CCE_M-1
  Determine and apply PA values for other CCEs:
  for i=M:(N-1)
    Step 1: Randomly and uniformly choose a PA_i value from PA set [-YdB ZdB]
    Step 2: Apply this PA_i values for CCE_i
  end