## Slide 1: Way forward on channel modelling for FD-MIMO
Samsung, MediaTek, Qualcomm
3GPP TSG-RAN WG4 Meeting #78
Malta, Malta, 15th -19th Feb, 2016
R4-161224

## Slide 2
2D antenna array model can be represented by , and total number of antennas is , where
  N1 is the number of antenna elements with the same polarization in the first dimension (Vertical direction)
  N2 is the number of antenna elements with the same polarization in the second dimension (Horizontal direction)
  P is the number of polarization groups.
Antenna labelling starts at different columns within the first row (N2), then goes through all the rows (N1), and at last for another polarization. I.e. labelling order following: first horizontal direction, then vertical direction and finally for another polarization group.
eNB 2D Antenna layout
4
10
6
12
5
11
1
7
3
9
2
8
Ntx = 12/(N1,N2,P) = (2,3,2)
5
13
7
15
6
14
1
9
3
11
2
10
8
16
4
12
Ntx =16/(N1,N2,P) = (2,4,2)
5
11
6
12
3
9
4
10
1
7
2
8
Ntx =12/(N1,N2,P) = (3,2,2)
7
15
8
16
5
13
6
14
3
11
4
12
1
9
2
10
Ntx =16/(N1,N2,P) = (4,2,2)

## Slide 3
Specify a correlation matrix for cross polarized 2D antenna arrays by following formula:
  where and is correlation matrix for antenna elements along first (Vertical) and second dimension (Horizontal) within the same polarization group.
  UE antenna correlation matrix and cross-polarization correlation matrix are same as before.
  Permutation matrix is same as before
  Correlation matrix for 2/3/4 Tx ULA antenna arrays with the same dimension and same polarization group at eNB side
The values for parameters α1, α2, β and γ for high spatial correlation
  The existing values α, β and γ for the high spatial correlation for cross polarized antennas can be reused in 2D antenna array, and candidate values were given in table below only the value of vertical direction correlation needs to be further decided.
  Decide Further decide final parameters for vertical direction correlation matrix (a1) in next RAN4 meeting.
Spatial Correlation Matrix
High spatial correlation |  |  | 
a1 | a2 | b | g
[0.9] | [0.9] | [0.9] | [0.3]
Note 1: Value of α1 applies when more than one pair of cross-polarized antenna elements in the first dimension at eNB side. Note 2: Value of α2 applies when more than one pair of cross-polarized antenna elements in the second dimension at eNB side. Note 3: Value of β applies when more than one pair of cross-polarized antenna elements at UE side. |  |  | 

## Slide 4
Apply beam steering for cross polarized 2D antenna arrays by following formula:
  is the steering matrix for both vertical and horizontal domains.
  is beam steering matrix for vertical domain with the same polarization group
  is beam steering matrix for horizontal domain with the same polarization group
  N1 corresponding number of antennas in vertical direction per polarization direction
  N2 corresponding number of antennas in horizontal direction per polarization direction
Beam-steering Approach
,