## Slide 1: Way forward on high speed BS demodulation assumptions
Nokia Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 Meeting #78 St. Julian’s, Malta, 15 – 19 February, 2016
Agenda Item: 6.6
R4-161255

## Slide 2: WF on Simulation Assumptions for PUSCH with ETU600
Simulation assumptions for PUSCH with ETU600
Parameters | Value
Propagation conditions | ETU600
# of TX antennas | 1
Antenna correlation | Low
Noise model | AWGN
Channel bandwidth (MHz) | 10
Number of PRBs | Full PRB allocation depending on BW
Cyclic perfix | Normal
Maximum number of HARQ transmissions | 4
RV sequence | 0, 2, 3, 1, 0, 2, 3, 1
Uplink-downlink allocation for TDD | Configuration 1 (2:2)
Channel estimation | Practical channel estimation
Simulation length | >= 10000 subframes

## Slide 3: WF on FRC
For QPSK 1/3, reuse current FRC table in TS36.104
For 16QAM rate 1/2, new FRC table shall be defined.