## Slide 1: WF on Coexistence Standalone
Ericsson, Huawei, Nokia, ZTE, Intel
3GPP TSG-RAN WG4 Meeting #78 R4-161295
Malta, Feb 15-19, 2016

## Slide 2: Background
This contribution captures the current status and first conclusion of NB-IOT standalone coexistence during RAN4#78 in Malta.
It also lists next steps related to coexistence.

## Slide 3: Coex results
Criteria:
  LTE:
    Throughput loss <= 5% (average and 5%)
  UMTS:
    Outage <= 5%
  GSM:
    Outage <= 5%
  NB-IoT:
    SNR loss < 1(?) dB (at 5%?, Average?, 95%?)

## Slide 4: Results
GSM
  BS: ACLR: 40 dB ACS: 45-50 dB
    With ACLR=40, outage degradation in [4.1 – 2.9] %
    With ACS=45, loss in [2.8 – 0.4] dB
  UE: ACLR: 20 dB ACS: 30-40 dB
    With ACLR=20, outage degradation in [3.4 - 0.8] %
    With ACS= 30, loss in [2-0] dB

## Slide 5: Results
UMTS
  BS: ACLR: 40-45 dB ACS: 40 dB
    With ACLR=45, outage degradation in [3.27 – 0.34] %
    With ACS=40, loss in [0.7 - 0] dB
  UE: ACLR: >50 dB ACS:20-40 dB
    With ACS=30, loss in [1.4 – 0] dB
Note: The ACLR value mentioned above corresponds to ACLR_3 or ACLR_4, not ACLR_1.

## Slide 6: Results
LTE
  BS: ACLR: 40-55 dB ACS: 40-50 dB
    With ACLR=45, loss in [12.3 – 0.74]%
    With ACLR=50, loss in [6.7 – 0.38]%
    With ACS=45, loss in [1.3 – 0.1] dB
  UE: ACLR: 35-45 dB ACS:35-40 dB
    With ACLR=40, loss in [11.3 – 2.2] %
    With ACS=35, loss in [1.51 - 0] dB
Note: The ACLR value mentioned above corresponds to ACLR_3 or ACLR_4, not ACLR_1.

## Slide 7: BS UEM Mask(s)
MSR mask:
  200 kHz Foffset
Coexistence:
  Should be no issue:
    ACLR ~48-50dB (R4-160911, tbc)
Other not agreed masks:
  LTE Rel8 mask: ??

## Slide 8: UE UEM mask
3 candidates (from R4-160154 - Intel)
 | single-tone SEM | multitone SEM | ACLR | SEM type
Option 1 | GSM | relaxed GSM | NO | relative
Option 2 | NB-IOT SEM (LTE like) |  | YES | absolute
Option 3 | NB-IOT SEM (GSM like) |  | YES | absolute

## Slide 9: Preliminary conclusions
Assuming ACLR and ACS values from previous slides,
Assuming mentioned impacts in previous slides,
NB-IoT can coexist with GSM, UMTS and LTE.

## Slide 10: Next steps
BS and UE RF specs expect ACLR/ACS value from coexistence (ref to associated WF).
Coexistence results are inputs to those requirements.

## Slide 11: Annex
Achievable power ratio is provided based on the candidate SEM proposed in [1, 2]
[1] R4-77AH-IoT-0059, “NB-IOT UE RF aspects”, Nokia Networks
[2] R4-160616, “On UE emission requirement for NB-IoT”, Huawei

## Slide 12: UE SEM requirements
UE SEM variants

## Slide 13: Achievable power ratio
Achievable power ration for coexistence by integral of the candidate UE SEM variants
[1] R4-77AH-IoT-0059, “NB-IOT UE RF aspects”, Nokia Networks
[2] R4-160616, “On UE emission requirement for NB-IoT”, Huawei
Protection over the 200kHz channel with edge to edge frequency offset | 100kHz (with GSM) | 500kHz (with LTE) | 580kHz (with UMTS)
(reference) GSM | 36dB | 60dB | 60dB
LTE like [1] | 18dB | 55dB | 55dB
GSM like [2] | 26dB | 50dB | 50dB