## Slide 1: 3GPP TSG-RAN WG4 Meeting #78 R4-161381 St. Julian’s, Malta, 15 – 19 February, 2016
WF on eMTC RF requirements
Ericsson, Verizon, Intel, Nokia Networks, AT&T, Alcatel Lucent, Sony, Qualcomm, NTT DoCoMo

## Slide 2: Background 1
In the WF for UE RF requirements for Rel-13 MTC [R4-156849] it was agreed:
  In the next meeting,
    Confirm if anyone of following requirements can be reused for each CBW (not only 1.4MHz but also other CBW) for Rel-13 MTC.
      ACLR
      SEM
      Spurious requirements
      transmit signal quality
    MPR needs to be further studied taking LO returning aspect into account.
    A-MPR needs to be revisited based on new power class.

## Slide 3: Background 2
In Way forward on RF requirements for eMTC [R4-158355] it was agreed that:
  eMTC UE requirements will be defined assuming that eMTC UE always transmits and receives up to 6RB within any system bandwidths.
  For eMTC UE, it is assumed that the LO is located at the center of the 6RBs
  For eMTC UE, for in-band emissions, the existing requirements applied to transmission bandwidth of 1.4MHz BW shall be used as a baseline.
In [R4-157668] it was agreed that
  The Rel-12 REFSENS numbers for Cat 0 with 1.4MHz system BW should be used as REFSENS requirements for all bandwidths in Rel-13
  REFSENS requirements for Rel-13 MTC UE can be applied for both normal coverage and enhanced coverage mode
  The approach is the same for both full duplex and half duplex mode, i.e., re-use the 1.7dB relaxation due to single RX for HD-FDD used in rel-12 for bands defined for 1.4MHz BW.
UE REFSENS requirements were agreed and CR [R4-158435] was endorsed

## Slide 4: Background 3
In WF for eMTC RF requirements [R4-77AH-IoT-0155] it was agreed:
  eMTC UE ability to meet all emission requirements (e.g. SEM, ACLR, spurious emission, in-band emission) will be checked for the next meeting
  For each system BW per band supported for eMTC:
    Study MPR against requirements as defined with respect to each system BW, for the edge RB position
    The guard band depends on the system BW
    Study A-MPR based on the outcome of MPR results
  No new emission table will be written for eMTC UE.
  Companies are encouraged to submit simulation results for the Power Class 3 and Power Class 5 UE in order to evaluate MPR and A-MPR

## Slide 5: Background 4
Work item exception for Further LTE Physical Layer Enhancements for MTC [RP-152217] states the following as the only remaining RF issue for eMTC:
  UE RF transmitter requirements for system bandwidth of 3MHz and above, and for both 23dBm and 20 dBm maximum output power
MPR requirements for Rel-13 eMTC is agreed in R4-161379

## Slide 6: Proposal
A-MPR requirements for NS07 according to WF R4-161380 is agreed in this meeting
The related CR (R4-160641) that includes both MPR and A-MPR is approved
RAN4 RF core part of Rel-13 eMTC is finalized
ACS requirements can be revisited in the next meeting under TEI