## Slide 1: Way forward on UE performance requirements for FD-MIMO
Samsung, Qualcomm, Ericsson, Intel
3GPP TSG-RAN WG4 Meeting #78
Malta, Malta, 15th -19th Nov, 2016
R4-161422

## Slide 2
Introducing PDSCH demodulation test case to verify DMRS enhancement
  Reusing existing TM-9 MU-MIMO test parameters as the baseline to introduce the test case.
  FFS for test applicable applicability.
Introduce PMI test cases for Class A
  Test Metric：
    Reuse existing PMI test metric, relative throughput ratio between follow PMI and random PMI under FRC test.
    Follow PMI and random PMI need to be restricted to the codebook and rank informed by the RRC parameters. Rank is based on CSR.
  Test case list：
    Totally 2 test cases are introduced for CSI class A with one single PMI test case and one multiple PMI test case.
    One test case is for 12 CSI-RS ports and another one is for 16 CSI-RS ports.
  Detailed test parameters:
    At least agree candidates on MCS, rank, codebook parameters, propagation channel by e-mail discussion so that all the companies can run the simulations for the next RAN4#78bis meeting to speed up the progress.
UE performance requirements 1/2

## Slide 3
Introduce CRI test case for Class B K>1
  Test methodology
    Option 1: One throughput test with single CSI-RS resource and another throughput test with multiple CSI-RS resources.
      Alt.1: Check both CRI statistics and throughput ratio.
      Alt.2: Check throughput ratio only.
    Option 2: One throughput test with multiple CSI-RS resources and check CRI statistics.
    Other options will not be precluded.
  Beamforming model
    Option 1: Dynamic power scaling
    Option 2: CSI-RS resource specific beamforming and beam steering channel model
Introduce PMI test case for CSI Class B K=1 with PMI-Config 1
Verify channel and interference measurement restriction functionality to verify following NW configuration when performing CSI measurement
Test cases are introduced only for FD-MIMO + 2Rx in Rel-13 timeframe
UE performance requirements 2/2