## Slide 1: WF on DL Control Channel IM for Asynchronous networks for PDCCH/PCFICH/PHICH and ePDCCH
Ericsson, NTT DOCOMO, Intel Corporation, ZTE
3GPP TSG-RAN WG4 Meeting #78 Malta, Malta, 15th-19th Feb, 2016
Agenda Item: 6.4.2
R4-161423

## Slide 2: Way Forward
Sufficient gain can be obtained by PDCCH/PCFICH/PHICH and ePDCCHby using LMMSE-IRC receiver compared to LMMSE-MRC receiver for asynchronous networks from companies results
Introduce test for the DL control channel IM receivers in the asynchronous networks for both PDCCH/PCFICH/PHICH and ePDCCH.
Candidate reference IM receiver for both PDCCH/PCFICH/PHICH and ePDCCH for asynchronous networks is LMMSE-IRC

## Slide 3: Simulation Assumptions (1)
Interference model for asynchronous network scenarios
  Rel-11 Type A receiver asynchronous interference model (TS 36.101 B.5.2, 8.2.1.2.4)
    Time offset: 1/3 and 2/3 subframes as timing offset for the 2 NCs
    Frequency offset: 0 Hz between all cells
Companies are encouraged to bring simulations in the next RAN4 meeting for the following test cases to for alignment purpose
The results are expected to be provided for the following reference receiver structures
  LMMSE-MRC, LMMSE-IRC
# | Control channel | INR | Network Type | Duplexing
1 | PDCCH / PCFICH | High | Asynchronous | FDD
2 | PHICH | High | Asynchronous | FDD
3 | ePDCCH | High | Asynchronous | FDD

## Slide 4: Simulation Assumptions (2)
Parameters | Value
System bandwidth | 10MHz for both serving cell and interfering cells
Duplexing mode | FDD
Cyclic prefix | Normal
Number of interference cells | 2 interfering cells
Cell id | Non-Colliding CRS: Interferer cell #1 - 1, Interferer cell #2 – 6
Interference power profile | High INR: I1/Noc = 13.91 dB, I2/Noc = 3.34 dB
Network synchronization scenarios | Time offset: 1/3 and 2/3 subframes as timing offset for the 2 NCs Frequency offset: 0 Hz between all cells
CRS ports | Port 0 and 1
Antenna configuration | 2x2 with Low correlation
Tx EVM | 6%
Unused Serving cell RE-s and PRB-s | OCNG
Interference model for asynchronous scenario | Rel-11 Type A receiver asynchronous interference model (TS 36.101 B.5.2) Companies can provide results for additional scenarios
Channel model | EVA70
Number of PHICH groups (Ng) | 1
PHICH duration | Normal

## Slide 5: Simulation Assumptions (3)
Parameters | Value
PDCCH/PCFICH parameters | 
Serving cell PDCCH | AL 2, 4; DCI Format 2 (43 bits – FDD, 10MHz)
CFI | CFIS = 3, CFII = 3
Performance metrics | Pm-dsg vs SINR
PHICH parameters | 
PHICH FRC | R.19 in TS 36.101
CFI | CFIS = 1, CFII = 1
Performance metrics | Pm-an vs SINR
EPDCCH parameters | 
Serving cell EPDCCH | FRC #1: AL 2 Localized EPDCCH FRC #2: AL 4 Distributed EPDCCH DCI Format 2C (44 bits – FDD, 10MHz)
Number of PDCCH symbols and EPDCCH start | CFIS = CFII=2, EPDCCH starting symbols is derived from CFI
EPDCCH parameters | Number of EPDCCH Sets Configured = 1 Distributed EPDCCH set PRBs {3, 17, 31, 45} Localized EPDCCH set PRBs {0, 7, 14, 21, 28, 35, 42, 49} EPDCCH is transmitted in all subframes EPDCCH precoding model is in accordance to TS 36.101 B.4.4. and B.4.5
Performance metrics | Pm-dsg vs SINR