## Slide 1: Way forward on performance metric for V2V system
Agenda item: 7.13.1
Source: CATT,…
3GPP TSG-RAN WG4 #78bis R4-161678
San Jose del Cabo, Mexico, 11 – 15 April, 2016

## Slide 2: Background
In RAN4#78 meeting, it was agreed that evaluation metric for the V2V victim scenarios needs further discussion.

## Slide 3: Performance metric
Adopt the Packet Reception Ratio (PRR) defined in RAN1 TR36.885 as performance metric for V2V system in RAN4 co-existence simulation study.
PRR is determined with the SNR VS. BLER mapping table and/or curve. RAN4 should use the same baseline mapping model in order to align system simulation results.
It is proposed that companies provide link level simulation results for the mapping model based on assumptions in next slide.

## Slide 4: Tentative link level simulation assumption
Parameter | Assumption
Bandwidth | 10Mz
Carrier frequency | 2.0G for licensed band
Number of antenna | 1 TX and 2 RX
Fading | The same as ITU-R UMi clustered delay line models (CDL) used in TR36.843
channel | LOS &NLOS
Modulation | QPSK
Coding | Turbo,1/2
TBsize | 300byte
Number of Occupied PRB | 16
Relative speed | 30km/h
Retransmission | Off
The maximum transmission number | 1
synchronization | Ideal (no Synchronization error impact in the simulation)